## Slide 1: Detecting Distant Drawdowns with Water-Level Modeling
Keith J Halford, Carson City, NV
Tracie Jackson, Henderson, NV
SeriesSEE Workshop, 2020 NWRA Annual Meeting
Tuesday, February 11, 2020, Las Vegas, NV

## Slide 2: ER-6-1 #2, Yucca Flat
Southern Yucca Flat
Carbonate rock
T = 100,000 to 250,000 ft²/d
  Assumed width affects T
  Multi-well aquifer test
  525 gpm for 90 days
Drawdowns detected
  ER-7-1 > 6 miles
  UE- 7nS > 8 miles
2 MILE
ER-6-1 #2
ER-7-1

## Slide 3: Drawdown Detection
Water levels ER-7-1
  Fluctuate 0.5 ft
  Pumping effects ambiguous till 6th day
Fit synthetic water level to antecedent data
Drawdown is synthetic minus measured
  Clear signal less than 1 d
Overwhelm noise by pumping 90 days
Aquifer
Test
2004

## Slide 4: Bigger Picture
Tracer Well complex
  Drilled late 1960’s
  Aquifer test 1975
  T = 90,000 ft²/d
Barometer & tides
  Pronounced effects
Pumping likely, but small drawdowns
20 MILES

## Slide 5: Well TR-3 & Pumping
Water-level fluctuations in TR-3
  Barometric changes, earth tides, & seasonal trends
Detectable drawdown response in record
  Army 1 and ER-6-1 #2 about 12 and 33 miles away

## Slide 6: Water-Level Modeling
Sum possible sources
Natural signals
  Tides
  Barometer
  Background water levels
Natural components can be correlated
Pumping
  Superimpose Theis
  Transform function
  T & S limited to no value
Theis Transform
Synthetic water levels

## Slide 7: Water-Level Modeling
Fit measured water levels
Adjust amplitude and phase each series
Drawdown = Theis Transform - Residuals
-0.5
0.0
0.5
1.0
1.5
04/08
04/15
04/22
04/29
05/06
05/13
05/20
05/27
06/03
06/10
WATER LEVEL CHANGE, IN FEET
Theis Transform
Pumping
EarthTide
GravityTide
Barometer
Barometer Avg 1d
Barometer Avg 7d
Background
Background Avg 1d
Synthetic
Measured
Drawdown

## Slide 8: TR-3 Water-Level Models
Barometer & tides only
Kink shows missing component
ER-6-1-2
2003
WL Model
Army 1
WW-C-1
2004
WL Model
RMS=0.01 ft
RMS=0.03 ft
Water-Level Change (ft)
Water-Level Change (feet)
2003 2004 2005
Pumping (GPM)

## Slide 9: 3-Year Analysis
Barometer & Tide
Residuals biased without pumping
Barometer, Tide, & PUMPING

## Slide 10: ER-6-1 #2 Distinct
Army 1, WW-C-1, & ER-6-1 #2 affect TR-3
Detection possible because of ER-6-1 #2
  Intense pulse
  Brief & unnatural
Army 1
  Greater cumulative effect
  Not unique till 2005 – 2006
Theis T & S
  Consistent with TR-3 results
  Account for geometry
WATER LEVEL CHANGE, IN FEET
Q, GPM

## Slide 11: Tracer 3 Drawdown
Drawdown just response to ER-6-1 #2 pumping
Response constrains T & S south of Yucca Flat
Qualitatively supports thin, high diffusivity paths
Best fit ~ 0.01 ft >> RMSDaily-Theis = 0.009 ft

## Slide 12: Analyzed Wells
Dozen wells interpreted
  Detected in 7 wells
  No detection in 5 wells
Detection limit differs
  ~0.05 ft for transducers
  ~0.5 ft for tape downs
Interpret hydraulic properties with numerical model

## Slide 13: Investigated Area
ER-6-1 #2 MWAT affected large area carbonate rocks
Measured drawdowns informed T & S estimates in DV3 regional model
Tracer 3 response shows scale affected
Supports megachannel
15 MILES
0.05 ft
0.02 ft
0.02 ft
0.05 ft
Jackson and Halford, 2019

## Slide 14: Detected
Multiple detections in Yucca Flat
Rapid attenuation to east, ER-3-1-2
Tracer 3 is 33 miles from ER-6-1 #2
15 MILES

## Slide 15: Conclusions
Water-level modeling
  Differentiate environmental fluctuations & pumping effects
  Shrink threshold for detecting drawdown, 0.03 – 0.05 ft
SeriesSEE—Water-level modeling software
  Excel Add-In, Uses FORTRAN codes & PEST for speed
  Quickly process drawdown estimates
Greatly expand investigated volume of aquifer tests
  Test across faults and structures
  Pumping signals detectable in transmissive units