## Slide 1: SeriesSEE an Excel Add-In ————————— Graph, Filter, & Analyze Time Series or Geophysical Logs
Keith J Halford, Carson City, NV
Tracie R. Jackson, Henderson, NV
SeriesSEE Workshop, 2020 NWRA Annual Meeting
Tuesday, February 11, 2020, Las Vegas, NV

## Slide 2: SeriesSEE
Excel Add-In
  Always accessible
  Handles non-numeric entries
View
  More than 8,000 series
  Magnification tools
Filter & Clean
  Global rules, graphical selection, gap filling
  Track changes
  Original data not altered
Analysis
  Subtotal, PolyFit, SimpleQ
  Water-Level Modeling

## Slide 3: Data Format
Series hang from header—1 row
  Multiple time columns
  Intervals can differ
Time headers must be identical
Defined by upper, left corner entry
Select cell in data before creating viewer

## Slide 4: Time Series Analysis
View series
Determine series to analyze
  Identify potential drawdown
  Select background series
Clean necessary series
Clip data to selected period

## Slide 5: Subtotals or Bins
Reduce data by fixed periods
  Average, Std. Dev.
  Min., Max.,
  Count
  Sum
Results—New workbook
  New data set
  Append to old
  Discard

## Slide 6: Offset
Changes obscured by
  Differing depths to water
  Water level altitudes
Offset shifts selected series so
  First value,
  Average,
  Minimum, or
  Maximum equals 0
Y-axis spans just observed fluctuations

## Slide 7: SimpleQ
Simplify pumping
  Reduces changes
  Reduces schedule
Step-wise pumping
  Graphical display
  Water-level modeling
Subtotals
  Compare with original

## Slide 8: Polyline Fitting
Improve parameter estimation
Original flow log
  Noisy
  More than 5800 pairs
  Impossible reversals
Bin to 5-ft intervals
  Reduces to ~230 pairs
Fit polyline sequentially
  Add pairs
  Minimize differences
Monotonic Q change
Weights flow change

## Slide 9: Documentation
Techniques & Methods
  Folder: T+M_SeriesSEE
Add-In installation explained
All functions are listed
Sequence is similar to menu structure
Help menu

## Slide 10: SeriesSEE, an Excel Add-In
You want it because, easy & painless
Report & software available online
USGS Publications Warehouse
http://pubs.usgs.gov//tm/tm4-F4/