## Slide 1: Water-Level Modeling Theis Transforms
Keith J Halford, Carson City, NV
Tracie R. Jackson, Henderson, NV
SeriesSEE Workshop, 2020 NWRA Annual Meeting
Tuesday, February 11, 2020, Las Vegas, NV

## Slide 2: Other Signals
Well WW4a pumps
Analyze response in well WW4 at Nevada Test Site, r = 1,200 feet
Dual-porosity response clearly present
1200 FEET

## Slide 3: Noise & Interpretation
WW4a is production well, cycles to fill tank
Repeat pumping, should repeat responses
Interesting responses unrepeatable
Earth tides & barometric effects bulk of “interesting” responses
Monitor much more than pumping period
http://nevada.usgs.gov/water/AquiferTests/ww4a.cfm?studyname=ww4a

## Slide 4: Environmental Fluctuations
Water levels fluctuate
  Barometric change
  Earth tides
  Seasonal trends
Barometer affects vented transducers too
  +2,000-ft unsaturated zone
  Diffusion to water table affects water levels
Magnitude of Fluctuations
  Daily, 0.1 to 0.5 ft
  Monthly, more than 1 ft

## Slide 5: Drawdown Detection
Estimate drawdown
  Great distance
  Adjacent aquifers
  High transmissivity
Detecting small changes difficult
Requires water-level modeling
PUMPING
PERIODS

## Slide 6: Water-Level Modeling
Sum possible sources
Natural signals
  Tides
  Barometer
  Background water levels
Natural components can be correlated
Pumping
  Superimpose Theis
  Transform function
  T & S limited to no value
Theis Transform
Synthetic water levels

## Slide 7: Synthetic Water Levels
is a constant, L
n is the number of time series components
is the time series component
is the amplitude multiplier of the ith component, L
is the phase shift of the ith component, T
is the value of the ith component at time
All series interpolated ► Functions are smooth
Estimated

## Slide 8: Water-Level Modeling
Fit measured water levels
Adjust amplitude and phase each series
Drawdown = Theis Transform - Residuals
-0.5
0.0
0.5
1.0
1.5
04/08
04/15
04/22
04/29
05/06
05/13
05/20
05/27
06/03
06/10
WATER LEVEL CHANGE, IN FEET
Theis Transform
Pumping
EarthTide
GravityTide
Barometer
Barometer Avg 1d
Barometer Avg 7d
Background
Background Avg 1d
Synthetic
Measured
Drawdown

## Slide 9: Step-Wise Fitting
Fit each component & scale to initialize
Model natural fluctuations & project
Model whole period – no pumping component
Add Theis Transform
Pumping
Theis Transform
Fitting Period
Fitting Period

## Slide 10: Multiple Theis Transforms
Multiple transforms, 1 pumping schedule
  Multiple T & S
  Fast, slow, other
  Assists sign challenged
Residuals capture deficiencies
Drawdown is sum,
  Theis transforms &
  Residuals
RMS = 0.005 ft

## Slide 11: Many Averages
Multiple components
  Diurnal fluctuations
  Regional trends
  All captured in record
Separate components
  Repeat data series
  Apply different moving averages
Estimate amplitude & phase of each
Solvable
  Tikhonov regularization
  Weak constraint

## Slide 12: Non-Unique, Non-Problem
Explain water-level changes near perfectly
BUT, solution non-unique
  Scads of parameters
  Estimates affected by initial values
Not a problem
Synthetic water level is result of interest
  Drawdowns
  Environmental Changes
So What!

## Slide 13: Cyclic Noise Example

## Slide 14: Colorado River Example
1,000 FEET
200 FEET
72 gpm
Migration & Remediation
2 aquifer tests
  Pumped volume limited
  Less than 20,000 gal
  Small drawdowns
Colorado fluctuates
  Daily dam releases
  3 ft range
  Difficult quantifying drawdown
72 gpm