## Slide 1: Water-Level Modeling Complex Geology
Keith J Halford, Carson City, NV
Tracie R. Jackson, Henderson, NV
SeriesSEE Workshop, 2020 NWRA Annual Meeting
Tuesday, February 11, 2020, Las Vegas, NV

## Slide 2: Hypothetical Model
Pahute Mesa Conceptualization
1 pumping well
4 observation wells
Simulated over 5 months
4 stress periods
  2 pumping, 2 recovery
  Pumping rates of 1500 m3/d
  10 day pumping periods
Documented in article

## Slide 3: Cross Section
Discrete blocks of aquifer and confining units
Fault displacements of more than 500 m

## Slide 4: Hypothetical Drawdown
“Known” drawdown extracted from 4 locations
“Measured” water levels =
  known drawdown + measured noise (background well)

## Slide 5: Compare Drawdown
Theis transform within 0.012 m of known maximum
Matches well throughout recovery
Known drawdown
Garcia, C.A., Halford, K.J. and Fenelon, J.M. (2013), Detecting Drawdowns Masked by Environmental Stresses with Water-Level Models. Groundwater, 51: 322–332.

## Slide 6: More Complex Geology
Sheath
Core
100 FT/D
0.05
Hydraulic Conductivity
Simulate drawdown
  Layered system
  Across faults
  Displace units 1200 ft
“Realistic” faults
  Permeable sheath
  Low-K cores
Pumping
  500 gpm
  Two 10-d periods
Fit Theis transforms to extracted drawdown

## Slide 7: Noise Limits Estimate
Known drawdown, O8
Theis assumptions
  Grossly violated
Estimate w/ noise added
  RMS-fitting = 0.013 ft
  RMS-predict = 0.020 ft
Fit 2 Theis transforms, pure MODFLOW output
  RMS-fitting = 0.0005 ft
  RMS-predict = 0.0005 ft
Theis transforms are fine

## Slide 8: Not Correlated
Environmental fluctuations
  Barometer
  Background WLs
  Tides
Correlation exists
  Theis parameters
  Tidal parameters
Not between Environmental fluctuations & pumping signal

## Slide 9: HypoFrame—Appendix D
Do it yourself workbook
  Simulate aquifer tests
Hypothetical aquifer system
  Flat-lying geologic units
  2 intersecting faults
  Vertically displaceable quadrants
Aquifer test
  Complex pumping schedule
  Define wells & placement
Workbook
  Creates MODFLOW 2005 model
  Adds noise to MNW output
  SeriesSEE input created

## Slide 10: Other Applications

## Slide 11: Micro Met Data
Extrapolate to site
  Partial record at site
  Full record at other site
Regress overlapping data
  Cloudy
  Poor storm prediction
Model wind speed w/ WLM
  Wind speed from other site
  Day, night, & storm series
  Moving averages 0 – 12 hr
  RMS reduced 3X
Greater wind speeds
  WLM scatters less than linear regression

## Slide 12: Gapfill Micro Met Data
Model precipitation and diurnal fluctuations
Fit each series and minimize error
Project fit
Fitting Period
Projection Period
RMS = 17 W/m2

## Slide 13: Estimate Q—Tidal Creek
Estimate Q in Crawford Creek from continuous gage
Tools exist to shift scales easily in WLM
Amplitude 17% of primary, Phase shift half-hour
Extrapolate record with WLM, or …
1 MILE
“There is something fascinating about science. One gets such wholesale returns of conjecture out of such a trifling investment of fact.”
― Mark Twain, Life on the Mississippi

## Slide 14: Pahute Mesa Example

## Slide 15: Pahute Mesa
Groundwater flows through volcanic–rock aquifers and confining units
Radionuclides migrating downgradient
Major fault structures
Multiple-well aquifer tests
  130 – 320 gpm
  3 – 10 d periods
~20 observation wells
Background wells
Search: USGS Nevada Aquifer Test
1 MI
Fault Structure
ER-EC-11
ER-20-8
ER-20-7

## Slide 16: Drawdown Estimates
Estimated drawdown
Fits: 0.004 – 0.02 ft
Detection:Max ≥ 0.04 ft
Classify
  Detected
  Undetected
Certain detection
  63 well pairs, 7 tests
  ―――――――――
Are detections false?
1.3 mi
1.4 mi
1.7 mi

## Slide 17: Expanded Volume
Pumped ER-EC-13
2 aquifer tests
  Upper zone, 8E6 gal
  Lower zone, 6E6 gal
Detected 2-3 miles
Maximum drawdown
  ~1 inch
High confidence in results
  Repetition w/ 2 tests
  Antecedent & recovery data, lots
ER-EC-13
Upper &
Lower
6 MILES
http://nevada.usgs.gov/water/AquiferTests/ER-EC-13_MUZ_MLZ.cfm?studyname=ER-EC_13_MUZ_MLZ

## Slide 18: WLM Example
Pahute Mesa, NNSS, Nevada
  Radionuclide transport
Extensive drilling & aquifer testing
  2008 to 2014
Thick volcanic rocks
  Between calderas
  Displace > 1,000 ft at fault structures
ER-20-5-3, Observation well
ER-20-7, Pumping well
1 MILE
Background well

## Slide 19: Cross Section
Complex, volcanic geology—not homogeneous, isotropic, etc.
Deep water table ~ 2,000 ft—Pervasive barometric effects
ER-20-7
ER-20-5-3

## Slide 20: Go to Workbook
Estimate drawdowns in well ER-20-5-3 with SeriesSEE
http://pubs.usgs.gov//tm/tm4-F4/