## Slide 1: Effects of Well and Piezometer Design on Water-Level Monitoring
MODIFIED FROM –––
2017 NWRA Annual Conference, Reno, NV
Technical Session D:Water Levels and Well Design
Thursday, February 16, 2017

## Slide 2: Short / Long Screens
Short screens <20 ft and piezometers
  Discrete interval, point
  Head and QW differences observable
  Minimally disturbs flow system
Long screens >100 ft
  Integrates head and QW
  Head skewed towards most transmissive interval
  Well passively induces flow between units
  QW skewed towards interval with higher head
Bias towards short screens
  Reduce apparent risk of contaminant migration
  Less likely to observe water-level changes

## Slide 3: Heterogeneity Effects
Homogeneous aquifer
  Drawdown similar with depth
  Screen position & length minimally affect observations
Heterogeneous aquifer
  Discrete fracture
  Proximity to transmissive feature controls drawdown
  Screen position & length greatly affect observations
Completion approach
  Prior knowledge
  Honest assessment of need
QOUT
Q, IN GPM
0
500
DEPTH, FEET
0
1000
500
Line of Equal
Drawdown

## Slide 4: Prior Knowledge
Surficial geology offers some clue
  Basin fill more predictable, than hard rocks
  Significant variability all units
Wells provide real knowledge
  Developed basin
    Short screens can work
  Undeveloped basin
    Hedge bets with long screen
    Embrace your ignorance
2 MILES

## Slide 5: Hard Rock
ER-6-1 #2, Yucca Flat, NV
  Open to 1,300 ft carbonate
  >90% of transmissivity, 2% of open hole
  Determined with flow logs & aquifer tests
Other indicators of transmissivity
  Not rock type
  Not fracture count
More likely to miss permeable interval with short screen
Dolomite
Vuggy
Dolomite
Fracture
Zone
Quartzite

## Slide 6: Basin Fill
W4-54, Antelope Valley, CA
  Open to 900 ft basin fill
  80% of transmissivity, 16% of open hole
  Determined with flow logs
Lithology & resistivity
  Clay & sand distinct
  Permeable sands similar to low-K sands
Short screen
  Better odds than hard rock
  Can still miss target

## Slide 7: Test Tradeoffs
Compare responses in hypothetical groundwater system
  Two distinct aquifers
  90% of transmissivity in shallow aquifer
Aquifer test
  Pump 500 gpm, 10 d
  Recovery observed, 40 d
Hydraulic properties
  Transmissivity, T = 8,800 ft²/d
  Specific yield, Sy = 0.1
  Specific storage, Ss = 2.E-6 1/ft
  Horizontal:vertical anisotropy = 10:1
E
W

## Slide 8: Lithology & Completions
Distribution from Pahute Mesa
  90% of T in <4% of >50,000 ft
Pump permeable interval
Observation wells
  1 and 2 miles from pumping well
  E-W short screens, shallow & deep
  N-S long screens, intersect all
E
W
S
N
Shallow
Deep
0.03 ft/d
10 ft/d
200 ft/d
T = 8,800 ft²/d

## Slide 9: Drawdown in Sections
Long screens affect drawdown, less so during recovery
  Increase likelihood of drawdown detection, Reduces detection limit
DEPTH BELOW WATER TABLE, IN FEET
0.5
0.1
FEET
TIME
PUMPING
DAYS
2,000 FEET
W
S
N
DETECTED
E
UNDETECTED

## Slide 10: 1 Mile Away
Sharp response in pumped, shallow unit
Attenuated & delayed in unpumped, deep unit
Long screen change similar to shallow, short screen
  Weighted towards unit with greater transmissivity
Maximum induced Q is 4 gpm in long well
500 gpm

## Slide 11: 2 Miles Away
Responses similar to 1 mi, Except half the change
Maximum induced Q <2 gpm in long well
  Minor effect on QW, long-term QW greater consideration
True detectability less clear than advertised
  Risk of non-detection greater than apparent
500 gpm

## Slide 12: Natural Fluctuations
Ideal drawdowns, natural fluctuations absent
Responses less clear combined with barometric change, tidal signals, & long-term trends
Drawdown recoverable with water-level modeling
500 gpm

## Slide 13: Estimated with WLM
Drawdown recoverable with water-level modeling
  Sensitive to measurement resolution
Vibrating wire installations—Grouted in-place or Avoiding thermal effects in pumping wells
  Greater pressures, Lower resolution
500 gpm

## Slide 14: Measurement Resolution
Drawdown estimable with water-level modeling
  Inherent noise remains in estimated drawdowns
  Low resolution reduces detection
Further explanation in upcoming SeriesSEE classes
  March 1, Las Vegas; June 19, 2017, Reno
500 gpm

## Slide 15: CONCLUSIONS
Hydraulic conductivity variable in most wellbores
  Transmissive intervals small fraction, <10% in carbonate & volcanic rocks
  Flow only definitive identifier of permeable intervals
Adapt wells to intended observations
  Short screens appropriately add detail,
    Developed basins with nearby stresses
  Long screens better in the absence of data
    Undeveloped basins with distant stresses
Monitor distant drawdowns with long screens
  More effective than multiple short screens
  Consistent with how smart we actually are

## Slide 16: End Section