## Slide 1: Application of Slug Test Analysis

## Slide 2: Naval Station Mayport
Characterize plumes from
  Waste oils, fuels, solvents, & paints
  Dumped 1942 to 1994
Many wells required
  Greater than 200 sites
  ~ 300 wells, Many nested
  Most 2” PVC, 10-ft screens
Dredge spoil comprises much of Mayport
  Shoreline & marshes filled
  Clay, silt, sand, & shells
  ~ 50 ft of aquifer above thick clays
1880
MARSH
(Halford, 1998)

## Slide 3: Mayport NAS, FL
Hydraulic diffusivity (T/S) estimated from tidal signals
  Signal propagates further as T/S increases
Hydraulic conductivity estimated, from many aquifer tests
  87 slug tests
  50 pumping aquifer tests
Compare K estimated from slug tests and pumping tests
  16 wells with both tests
  Estimate bias from slug tests
(Halford, 1998)

## Slide 4: Pumping & Slug Tests
Similar hydraulic conductivities from pumping & slug tests
Geometric means
  Pumping, 16 ft/d USGS
  Slug tests, 10 ft/d Consultants
Results differed minimally relative to uncertainty of estimates
Pumping aquifer tests investigated small volumes
  Q ~ 5 gpm, Pumping time ~ 3 hrs.
  Volume < 1,000 gal.
(Halford, 1998)

## Slide 5: Tuff Pile, Yucca Flat
(Halford and others, 2005)
Geopressured zone created by nuclear testing
Subsidence observed
  Point measurements
  InSAR images, Volumetric change
“Odd” hydrographs from wells in Tuff Pile
  Synonymous with tight rocks
  “Trivial” factors become visible
Nevada National
Security Site
Yucca Flat
1 MILE
N
InSAR
estimate of
hydraulic
conductivity
UE-4t 1

## Slide 6: Odd Water Levels
Well UE-4t 1 (1906-2010 ft)
  USGS 370556116025405
  Drilled October 1990
  Initial water level ~400 ft BLS
  Expected water level ~1,600 ft BLS, Prior to nuclear testing
Expect monotonic decline from nuclear testing effects
Water level rises after drilling
  2 years of rising water levels
  Interpreted as recovery from drilling
  Minor perturbation with more record
Slug
Test
Nuclear Testing Effect
y0

## Slide 7: Nuclear Testing & Water Levels
DV  DWL  R
Each nuclear detonation
  Compresses rock
  Reduces pore volume
  Increases water level
  “Instantaneous” rise
  Process occurs regardless of K
Water-level responses observed because of low K
  Big rise because water not squishy
  Low K delays equilibration
  van Noordbergum effect also caused by deforming low-K rocks
BOOM!
Notes: Similar to "Noordbergum effect“

## Slide 8: Slug Tests
Recovery from drilling in tight rocks
  Similar to slug test response
  Adjust concept of “instantaneous”
    Couple of weeks, fast in comparison
    Many months or years for recovery
Water-level change in casing is known volume
Awareness of background effects minimally effects K estimates
  Ignore decline, K = 8x10-7 ft/d
  Correct for decline, K = 4x10-7 ft/d
Ignore decline, K = 8.E-07 ft/d
Correct for decline, K = 4.E-07 ft/d

## Slide 9: InSAR & Slug Tests
Analyzed recovery in 9 wells
  Slug volumes, 40 to 50,000 gallons
  U – 2bs, Δy = 120 ft, dC = 99.5 inches, Emplacement hole
K estimates from recovery “slugs”
  Minimum 4x10-7 ft/d
  Maximum 3x10-3 ft/d
  Geometric mean 7x10-5 ft/d
K from InSAR = 1x10-5 ft/d
  30 to 40 million gallons
Median & mean slugs within order of magnitude of InSAR estimate

## Slide 10: Slug Test Advantages
Quick, cheap, and easy
  Many tests conducted and analyzed in a day
  Requires only 1 well
  Contamination issues are minimal
  Minimal equipment needs
    a slugging mechanism,
    pressure transducer, and
    a data logger
  Analysis and documentation are simple & fast
  Limited radius of investigation
  Test well development, compare rising & falling

## Slide 11: Slug Test Disadvantages
Hydraulic conductivity estimate uncertain
  Better than a poke in the eye
Transmissivity / K*bSCREEN influenced by:
  Completion & well-aquifer geometry
Limited radius of investigation
  Results from many wells give an idea
  Only feasible method if K*bSCREEN < 10 ft²/d

## Slide 12: Reporting & Documenting
Bare minimum in addition to estimate of K,
  Water-level response,
  Well / aquifer geometry, and
  Method of interpretation
Clear, concise, and consistent documentation is needed because slug tests tend to occur in large lots
Aquifer-test analyses packages and spreadsheets are useful tools
Analyze a site with a single, method (Bouwer & Rice, KGS, etc.)
  All methods are limited, K*bSCREEN = Fudge-factor * Slope
  Multiple methods does not address uncertainty, Creates needless noise

## Slide 13: End Section