## Slide 1: Aquifer Test Reporting

## Slide 2: Reporting
Aquifer-test results are interpretive
Good average typically, not overly precise
  1 significant figure is truthful
Cover basics & convince reader, “OK, these estimates are plausible”
Necessary parts listed & explained
  USGS OGW Technical Memorandum 2009.01 https://water.usgs.gov/water-resources/memos/

## Slide 3: USGS GW Memo 2009.01
Briefly describe test—Purpose, date, data collection procedures, and methods of analysis.
Sketch test site—Show wells & hydraulic features, streams, springs, ditches, other pumping wells
Report well construction & local geohydrology
Show complete time-discharge records—VOLUME PUMPED
Show hydrographs—before, during, & after pumping
Estimate drawdowns from water levels
Show plots of observed or adjusted drawdown data used to determine hydraulic characteristics

## Slide 4: Examples
Many aquifer tests reported in Nevada
  https://nevada.usgs.gov/aquifertests/index.html
Categorized by
  Study areas
  Method of Analysis
Freely use any analysis as a template
Search for
  USGS Nevada Aquifer Test

## Slide 5: Publish Results
Extensive aquifer testing at NTS during 1960s
  Searching for tight rocks beneath Pahute Mesa
  Do not want devices being drowned
Majority are slug tests on 200-ft intervals
  Packers isolate intervals in open hole
  Fill ~3 in. drill string to slug wells
  ~2,000 ft depth to water ► 700-800 gallons
  Slug tests frequently repeated in each well
Documented in technical letters & TEI reports
  Publications secretive, given nuclear connections
  Some results disseminated, PP-712B & PP-712C
  Most data and results not available

## Slide 6: Tales of the “Good Stuff”
Predicting contaminant transport of interest from early 1990s
  Renewed interest in old aquifer tests
  Multiple contractors over time
    UGTA started as <10 year project
    Project duration approaching 40 years
  Old data sets circulate among organizations
    Data sets get re-interpreted multiple times
    Documentation limited to an appendix, K perhaps in overstuffed report of >1,000 pages
“Process” leads to tales of 1,000’s of aquifer-test results being overlooked

## Slide 7: Example Packer Test
Well UE-19e (2730-2890 ft) example
  Tested interval
    Slugged twice
    Bailed once
    Three slug tests, Same well
Recovery frequently incomplete
  Mostly tight rocks under Pahute Mesa
Recovery curves replicate results
One unique transmissivity per well

## Slide 8: Clean-up from Fiction
Documentation & clean-up occurred
  Concerns existed, would “look bad” if “Good stuff” remained hidden
  Frus and Halford (2018) resulted
Greater than 5,000 analyses found
Reduced to 1,468 analyses after deleting duplicate files
  File & well names could differ between duplicates
  Results also inflated by analyzing each slug with multiple techniques
Ultimately, 360 unique T estimates

## Slide 9: References
AQTESOLV, 2025, Aquifer Testing Reference List, HydroSOLVE, Inc., http://www.aqtesolv.com/aquifer-tests/aquifer-testing-references.htm
Ferris, J.G.; Knowles, D.B.; Brown, R.H.; Stallman, R.H., 1962, Theory of aquifer tests, USGS Water Supply Paper: 1536-E, https://doi.org/10.3133/wsp1536E
Halford, K. J., Weight, W. D. and Schreiber, R. P., 2006, Interpretation of Transmissivity Estimates from Single-Well Pumping Aquifer Tests. Groundwater, 44:467–471, https://doi.org/10.1111/j.1745-6584.2005.00151.x
Halford, K., Garcia, C.A., Fenelon, J., and Mirus, B., 2012, Advanced methods for modeling water-levels and estimating drawdowns with SeriesSEE, an Excel add-In, U.S. Geological Survey Techniques and Methods 4–F4, https://doi.org/10.3133/tm4F4
Heath, Ralph C., 1983, Basic ground-water hydrology, USGS Water Supply Paper: 2220, https://doi.org/10.3133/wsp2220
Merritt, Michael, L., 2004, Estimating Hydraulic Properties of the Floridan Aquifer System by Analysis of Earth-Tide, Ocean-Tide, and Barometric Effects, Collier and Hendry Counties, Florida: USGS WRI Report 03-4267, https://doi.org/10.3133/wri034267
Neville, C.J. and van der Kamp, G. (2012), Using Recovery Data to Extend the Effective Duration of Pumping Tests. Groundwater, 50: 804-807. https://doi.org/10.1111/j.1745-6584.2011.00906.x
Stallman, Robert W., 1971, Aquifer-test design, observation, and data analysis, USGS Techniques of Water-Resource Investigation: 03-B1, https://doi.org/10.3133/twri03B1
USGS, 2009, Update on Guidance for the Preparation, Approval, and Archiving of Aquifer-Test Results, OGW Technical Memorandum 2009.01, https://water.usgs.gov/water-resources/memos/
USGS, 2025, Aquifer tests: Carson City, Nevada, U.S. Geological Survey, Nevada WSC, https://nevada.usgs.gov/aquifertests/index.html