## Slide 1: Observations and Wells

## Slide 2: PURPOSE
Aquifer tests should improve estimates of hydraulic properties
  Average transmissivity of an area at a minimum
  Storage coefficient with observation wells
  Heterogeneity with multiple observation and pumping wells
Test design should consider
  Properties of interest
  Uniqueness of hydraulic property estimates
  Well placement and stress distributions
Test design should NOT be constrained by analytical methods

## Slide 3: Constant Rate & Wells
Constant rate desirable
  Pump & observe with wells
Construction affects responses
  Wellbore storage
Skin defines all head losses
  Screen, gravel pack, & damage
Long well screens more likely to
  Detect drawdown, hydraulically connected
  Obfuscate vertical gradients
  Affected by aquifer heterogeneity
Be aware, Factors to interpret
Screenc
Gravel
Pack
Casing
Grout

## Slide 4: Well Volumes
Real wells are not line sinks
  Volume increases with diameter sq.
Significance relative to flow
Q increases, Volume an aside
(U-19bh)
98 inches
X 17 = 98 in. diameter

## Slide 5: Wellbore Storage
Refers to pumping well
First production from well
  Unit Vol. = casing – drop string
For example,
  Casing diameter = 8 in.
  Drop diameter = 4 in.
  Unit Volume = 2 gallons/ft
Significance increases
  Low pumping rate
  Low transmissivity
(Stoller-Navarro, 2006)
(Big Springs SW, Snake Valley, 2010)

## Slide 6: Orlando NTC
Remediate dry-cleaning spills
Sandy lithology with clay stringers
Characterize site with multi-well aquifer test
  Kx & Kz Upper zone
  Kx & Kz Lower zone
  Delineating plume also requires wells
Q = 52 & 39 gpm; drop after 3 min.
Bump in most drawdowns
Response in well 13-13B looks odd
(Halford, 1998)

## Slide 7: Observation Well Storage
Effect similar to reversed slug test
“Sudden” head decline in aquifer, well lags
Unconfined aquifer responds slowly, prolongs wellbore storage
Lag period increases as
  Well diameter increases— More storage
  Shorter screen— Less connection
  Cruddier completion— More skin
  Silt or clay lens — Less connection
TIME
(Halford, 1998)

## Slide 8: Effect on Results
Typical SS values for
  Water 1.4 x10-6 ft -1
  Aquifer ~2 x10-6 ft -1
Estimated SS ~10–100 x10-6 ft -1
  Approximates lag that is not simulated explicitly
Hydraulic conductivity unaffected
Packing-off well would negate lag, but impractical & harmful
Ignore meaningless SS estimates
TIME

## Slide 9: Long Well Screens
Well is not passive
Vertical gradients induce flow
Flow magnitude increases with
  Greater transmissivity (T) &
  Screen length
Water level weighted towards highest transmissivity
Interpret as if well completed in just transmissive material
K1
re
K1
K2
rw

## Slide 10: Confining Unit Wells
Well in aquifer “sees” same drawdown
Drawdown varies along screen from top to bottom in confining unit
Orientation and hydraulic properties exaggerate variability
Similar effects in fractured rock
  Drawdown propagates quickly in transmissive feature— Fractures
  Oozes away into tighter rocks— Undifferentiated host rock
Aquifer
Confining unit

## Slide 11: Flow in Observation Well
2,500 GPM
Spring
Valley
184W101, Spring Valley
Observation well 184W502M
  Temperature measured
  Transducer near water table
  Pumping changes temperature
  Change implies flow
Analytical solutions assume observations are not conduits
Analyze numerically
  Observation well simulated
  Induced flow ~ 40 gpm
https://nevada.usgs.gov/aquifertests/studies/tests.html?test_pg=spring_valley

## Slide 12: Flow in Observation Well
Numerical solution
  Explains flow in observation well
  Matches measured drawdowns
  T = 11,000 ft²/d
Compare drawdown from points to simulated observation well
  Quite different at water table
  Shape & magnitude okay at depth
Analyze analytically w/ Moench
  Compare at depth
  T = 10,000 ft²/d
Results materially not affected
Pumping
Well
Observation
Well
2000 ft
Columns
Rows
5
5
10
10
20
15
Drawdowns affected by well 184W502M
(Barlow and Moench, 2011)

## Slide 13: Offset Comparison
Example from Southwest Florida
  ROMP program
  Nested well clusters
  Characterize aquifers & confining units
Raised wells & shelters “solve” flowing well problem
Drawdown in pumping MW3
  Pumped 500 gpm from Suwannee limestone
  Measured drawdown greater than ideal
500 GPM
(Yobbi and Halford, 2005)

## Slide 14: Offset Comparison
Measured slope defines transmissivity
Ideal drawdown from model
  Theis is model in this example
  Real well losses not simulated
Measurements offset from ideal
  Well construction & partial-penetration
  Offset constant when flow is steady
Define offset after flow into well steady
  Minimal wellbore storage
  Converging flow to well established
  3 to 30 minutes after start of pumping
Avoids simulating head losses to production wells
(Halford and Yobbi, 2006)
Measured slope
Ideal Theis aquifer

## Slide 15: End Section