## Slide 1: Step Tests & Complications

## Slide 2: Step Tests
Primarily determines performance of pumping well
  Size production pump
For each step,
  Well pumped at constant rate
  Steady drawdown measured, ~2 hrs.
Increase pumping rate until capacity of pump or well reached
Measured drawdown at end of steps answers most questions
Transmissivity of aquifer estimable
  Slope of transformed drawdowns
(Rorabaugh, 1953)
Step | Q, GPM | Measured
1 | 1,600 | 58
2 | 2,500 | 94
3 | 3,500 | 133
4 | 4,000 | 155
1
2
4
3

## Slide 3: Well Loss Model
Model of drawdown modified,
  Add terms B´ & C for well losses
    B´, Linear well losses
    C, Turbulent, non-linear, losses
Other forms of well loss
  Replace C*Q² with C*Qⁿ,
    Estimate n too!
  Pick a set of fudge factors & Stick with them
T, B´, & C determined with multiple steps, minimum of 2
+ B´*Q + C*Q²
SKIN
(Rorabaugh, 1953)
)

## Slide 4: Petroleum Analysis
Transmissivity better defined by transformed time & drawdown,
  Both scales are meaningless
  Slope of steps should be parallel
  All overlay if no well loss or wellbore storage
Good diagnostic of T
Well loss model diagnostic plot
  Assume flowing intervals saturated
  > 100 ft of drawdown, Not necessarily
(Lee, 1982)

## Slide 5: Step-Drawdown Workbook
(Rorabaugh, 1953)
Pumping_StepDrawdown-2019.v3.xlsm
  Use Rorabaugh (1953) & Lee (1982)
  Revised Halford & Kuniansky (2002)
Added tools
  Display time series
    Identify analyzed data points
    Pumping superimposed on drawdowns
  Regress or manually fit data
    Manually estimating T necessary
    Parameter T can be fixed during regression
Simplified input & output
Report table drawdowns & efficiencies for each step

## Slide 6: Example

## Slide 7: REPORT TRANSMISSIVITY

## Slide 8: Transmissivity & K
Transmissivity
  Estimated quantity, not hydraulic conductivity
  Unknown thickness, Not a problem
  Aquifer thickness reasonable where, T greater than 500 ft²/d
Thickness, b, differs
  Depth Drilled
  Screen Length
  Model Thickness
Transmissivity estimate unchanged!
b
KBASIN FILL
KCARBONATE
CONFINING UNIT
T = K x b
K = T / b

## Slide 9: Interpretation of Transmissivity
Test with numerical models
  Transmissivity known
  Aquifer test duration of 2 days
Cooper-Jacob investigated by interpreting simulated drawdowns
Estimate 628 known transmissivities, with Cooper-Jacob
  Transmissivity 10 to 10,000 m²/d
  Specific storage 5 x 10-6 m-1
  Specific yield 0.05 to 0.3
  Vertical anisotropy 0.02 or 0.2
  Partial penetration 10% to 100%
(Halford, et al, 2006)

## Slide 10: Confined Aquifers
Transmissivity estimated from aquifer tests, K interpreted
Reduce transmissivity to K with aquifer thickness, T > 500 ft2/d
  K = T / bAQUIFER
  NOT screen length
Reduce transmissivity to K with screen length, T < 50 ft2/d
  K = T / bSCREEN LENGTH
  Volume pumped limited, Approaching slug test volumes
  Radius of investigation limited

## Slide 11: Unconfined Response
Unconfined response characterized by S-curve
  1st slope, Confined response
  2nd slope, Unconfined drainage
  Transition between 2 slopes
  2nd slope good estimator of T
Difficulties arise
  1st slope obscured by wellbore storage
  2nd slope not observed
  Partially penetrating well
  “Insufficient” duration or pumping rate
Ambiguity in best estimate
Wellbore
Storage
5 min.
1st slope, Confined
2nd slope, Unconfined

## Slide 12: CJ Estimates Unconfined
T more likely to be overestimated
Overestimation worst
  T of 300 – 3,000 ft2/d
  Average estimate ~3X greater
  Slope mechanistically estimated from 2nd day of drawdowns
Improve estimate with interpretation
  T greater than 3,000 ft2/d
  2nd slope visible
  Ignore transition data points

## Slide 13: Single-Well—Just T
Unconfined response can be matched with Moench solution
  Aquifer defined with T and,
    SS 1/ft,
    Vert. aniso,
    Sy
    Skin
Added terms non-unique, ignore
Transmissivity estimate
  Moench — 4,000 to 15,000 ft²/d
  Cooper-Jacob — 8,000 to 11,000 ft²/d
Transmissivity—GOOD, Report T
(Barlow and Moench, 1999)
Moench solution

## Slide 14: COMPLICATIONS

## Slide 15: Conventional Flow Logs
Measure tool & fluid velocity profiles
  Pump above screen
  Convert from velocity to flow rates
  Flow rates range from 0 to pumping rate
Interpret difference between pumped and unpumped well logs
Assume flow is horizontal
  Transmissivity  ΔQ
Except, Vertical flow does occur
  Partial penetration
  Well construction
  Encrustation / Fouling
QOUT
0
100
QIN
Difference between
unpumped &
pumped well
Profiles differ –– Aquifer unchanged
Q
70%
30%
0%

## Slide 16: Thermal Expansion
Geothermal Gradient
Celsius
Heated water column expands
  Coefficient ~ 0.0003 to 0.0005 C°-1
  Expansion lengthens water column
  Apparent water-level rise with transducer near water surface
Column is transducer to flow zones
Temperature change
  Average between pumping & geothermal gradient
Water level rises 1 ft
  1,000-ft column
  Average 3 C° increase
  Apparent potential decrease
Q
Homogeneous K
Fracture
Flow

## Slide 17: Pahute Mesa, NV
Define tritium plume beneath Pahute Mesa, NNSS
  ER-EC-11 wells, 1 of dozens
Pumped 300 gpm
  April & May 2010
  16 days
  5.6 million gallons
Temperature
  55 °C at depth
  T = 11°C @ water table
  Complex pumping schedule
2,000 feet
Transducers►
◄Pumped interval

## Slide 18: Thermal Noise – Pumped
ER-EC-11main, pumping well
  Well losses 120 ft
  Thermal expansion 10 ft
  Drawdown from pumping 5 ft
  Natural fluctuation < 1 ft
  Background change < 1 ft
Transmissivity, big & uncertain
  20,000 - 100,000 ft²/d
Models limited
  Heat & Flow
  Same diffusivity equations
Correction possible if temperature profile measured
Unsteady flow
Well losses
Correlated ►

## Slide 19: Thermal Noise – Monitor
Monitoring well ER-EC-11i
  Completed in pumping well borehole
Water levels in ER-EC-11i
  Thermal rise 3.3 – 3.9 ft
  Drawdown from pumping 0 - 1 ft
  Natural fluctuation ~ 1 ft
Q change complicates
  Pumping column varies
  Heating variable, Less correlated with flow
Measured profile would help

## Slide 20: Single Well Tests
Pahute Mesa, phase 2
  Planned single-well, aquifer tests
  Monitored other wells, just in case
Single-well test results
  Not definitive, where transmissive
  Thermal expansion, Obscured drawdown
Useful as multiple-well tests
  Usual noise in observation wells
  Drawdowns detected, 2 miles
  ER-EC-11, Tmulti-well = 12,000 ft²/d
(Garcia and others, 2017)

## Slide 21: Head Loss in Open Hole

## Slide 22: Turbulent Flow in Aquifer
Flow turbulent > critical velocity
  Reynolds number, Re > 1 aquifers
Convergent flow occurs in aquifers
  Water enters wells or conduits
  Approaches & discharges from spring
Turbulence in aquifer is an artifact
  Not prevalent, limited volumetric extent
  Peeking through wells
Well in highly transmissive aquifer
  Flow to well from a single fracture

## Slide 23: Interval Dependence
Interpretation depends on vertical distribution of flow
Homogeneous K, same for 1,000 ft
  v = 0.0003 ft/s, Re < 1
Fracture zone, 1 ft
  80% of transmissivity
  v = 0.03 ft/s, Re ~3500
Flow not horizontal
Directly measure flow
  All else is useless
QOUT
Q, IN GPM
0
500
DEPTH, FEET
0
1000
500
Horizontal Flow
Interpretation

## Slide 24: Interpretation
Fit to flow, drawdown, & T
Drawdown in pumping well
    Theis 0.2 ft
    Measured 8 ft
Laminar drawdown, 1 ft
Approximate turbulence
  5-ft drawdown simulated
Fracture transmissivity
  Horizontal flow < 30%
  Laminar ~ 50%
  Turbulent > 90%
LAMINAR

## Slide 25: Vertical Flow
High T – Small ∆Q possible with vertical flow
Paths diverge near well
Turbulent & laminar paths appear similar
Laminar –Vertical flow less
Plug approximation OK
    ∆HPLUG ~ 8 ft
    Critical Re 1 d’less
Turbulent & laminar heads differ within 100 ft of well
Critical
Radius
0.03 ft
0.3 ft

## Slide 26: Fractured Rock Interpretation
Turbulence can create head losses in open holes
  Likely to occur in fractured rocks
Flow logs are qualitative tools
  Fuzz exists for wells in basin fill
  Fractured rocks break horizontal flow assumptions
Interpret transmissivity of producing intervals as minimums

## Slide 27: End Section