## Slide 1: Using Transmissivity Estimates

## Slide 2: Applications
Predicting future performance of pumping well
  Straightforward results from aquifer testing, Usually step tests
Expand estimates of T at wells by correlating with specific capacity
  Pump 3,000 gpm from a well, Likely transmissive aquifer
  Well pumped dry in 10 minutes at 5 gpm, Likely tight rocks
  Empirical relation extends usefulness of knowing pumping rate
Estimate likely transmissivities for geohydrologic units
Constrain numerical groundwater-flow models
  Compare field estimates to comparable volumes in flow model
  Create awareness of field estimates at minimum

## Slide 3: Transmissivity from Specific Capacity

## Slide 4: Specific Capacity (SC)
SC = flow rate / drawdown
  Usually gpm/ft
  Time not specified
  Inexact, but prevalent
Reported by NDWR in well logs
  ~ 10% have useful information
Empirically estimate transmissivity
  T (ft²/d) = 380 * SC (gpm/ft), (Frus and Halford, 2018)
80% of T estimates from SC within 5X T from aquifer test

## Slide 5: Other Empirical Relations
Other empirical relations
  T (ft²/d) = 230 * SC (gpm/ft), (Thomasson and others, 1960)
  T (ft²/d) = 217 * SC1.124 (gpm/ft), (Yager and others, 2012)
Useful range of SC estimates limited
  SC < 0.3 gpm/ft, not an aquifer
  SC > 100 gpm/ft, very transmissive
  No practical differences where useful
Specific equation unimportant
  Slop in relation negates differences
  Use whatever makes others happy

## Slide 6: Death Valley System
Transmissivities
  Many aquifer tests because of nuclear tests
  140 aquifer-test results, incudes “slug tests”
Specific Capacity
  ~ 15,000 well logs, Mostly Pahrump
  ~ 4,700 SC reported, Mostly Pahrump
  ~ 350, Q > 30 gpm
  ~ 130 Useful estimates of transmissivity
Transmissivity sites mapped with
  KML_WritePoints.v3
  Attach links and images to mapped points
50 MILES

## Slide 7: Volume Sampled
Transmissivity is an integrated average property
  Volume sampled is defined poorly
  Volume sampled is proportional to volume pumped
  Estimating area from volume sampled
    Storage coefficient, knowable
    Drawdown extent, very nebulous
Scale volumes to known results
  Qualitative scaling
  Consistently applied with volume
Apply collection of T estimates
Big Springs SW
Snake Valley, NV
Mayport, FL
ER-EC-13
NNSS
Long
Canyon,
NV
Halford and Jackson (2020)

## Slide 8: Transmissivity & Geohydrologic units

## Slide 9: Hydraulic Conductivity & Geology
IDEAL
Class geohydrologic units to predict likely transmissivity or K
Ideal geohydrologic units
  Relative K between units known
  Small variance, hydraulically distinct
Actual geohydrologic units
  ~ 400 estimates
  Mean K contradicts expected order
  Units hydraulically similar
Problem classifications
  3 Volcanic units are similar
  KCONFINING UNIT > KAQUIFER
(Belcher and others, 2002)
ACTUAL

## Slide 10: Simplified Geohydrology
Simplified classification scheme can be supported
  Carbonate rocks most transmissive, but much is not
  Volcanic rocks anything; High T around lava flows, Low T for ash-fall tuffs
  Basin fill most predictable; Analysis largely ignores clay & salt facies
Minimal predictive utility, but conceptually consistent
Halford and Jackson (2020)

## Slide 11: Transmissivity-Thickness
Transmissivity not correlated with thickness, open interval or geo-unit
  Carbonate rocks & Volcanic rocks
    Open interval & geo-unit thicknesses differ
    Fracture flow dominates, where transmissive
  Basin fill — Correlation could exist
    Thickness classification ignores cementing
  Low-permeability rocks
    Transmissivity concept breaks
Resistivity/gravity surveys
  Identifying an unknown structure useful
  Refining thicknesses wastes money
(Halford and Jackson, 2020)

## Slide 12: Most Flow Shallow
Little transmissivity at depth
  Carbonate rocks
    27 transmissivity estimates
    Deep T targeted in 6 wells, 100% failure
  Volcanic rocks, Pahute Mesa
    Depth-dependent testing, 17 wells
    Deepest well UE-20f, 13,686 below land surface
  Basin fill
    Cementing increases with depth
Flow-log style shows cumulative T
Most transmissivity within ½ mile of water table
Frus and Halford (2018); Halford and Jackson (2020)
Limit of Flow

## Slide 13: Probability Estimates
Estimating probability of transmissivities by geohydrologic unit
  Expected transmissivities where aquifer tests absent
  Bounds likely range of transmissivities
Necessary stories for groundwater-flow models
  Hydraulic properties must be assigned everywhere in numerical model
  Geohydrologic fantasy fills >90% of any groundwater-flow model
Not useful where field estimates of transmissivity exist
  Uncertainty of site-specific aquifer test far less than generalized odds
  Volume investigated lost; 100 gallons way different than 100 million gallons

## Slide 14: Transmissivity Comparison

## Slide 15: Generalized vs. Site Specific
Hydraulic-conductivity limits indistinctly define likely T
  Bounding range of K for units
  Multiple units define simulated T
  Probabilities similar at all wells
  Low transmissivities excluded
Aquifer-test results unique
  Normal uncertainties from estimated slope & flow rate exist
  Probabilities retain differences between T at wells
  Sample simulated T to compare

## Slide 16: Simulated Transmissivity
GW model contains all information to calculate transmissivity around well
  Hydraulic conductivity — Kx distribution
  Contributing thicknesses—Grid dimensions
Sample volume defined with Threshold drawdown—Nebulous term
  Estimated with mini-numerical models OR
  Empirically related to pumped volumes
Simulated transmissivities
  Averaged laterally in each layer
  Layer averages summed vertically
Hydraulic Conductivity,
In feet per day
0.001
40
Drawdown, in feet
1
30
QOUT

## Slide 17: Identify Sample Volume
Simulate drawdown from aquifer test with mini-model
Sweep mini-model drawdown through regional model grid
  Identify cells in sample volume
  Assign fractional contribution to simulated transmissivity
Write information for sampling simulated transmissivity while calibrating regional model
Method documented in T-COMP
(Halford, 2016)

## Slide 18: Get Comparison
List of cells & fractions created
Compute transmissivities in cells
Sum transmissivities times fraction for all contributing cells
  Fractions sum to 1 in each layer
Write simulated transmissivity & log(T)
  Compare log(TMEASURED) to log(TSIMULATED)
Variability can exist in sample
Less wrong than not comparing T
TRANSMISSIVITY, IN
FEET SQUARED PER DAY
Notes: c Program T-COMP_Simulated.f -- Extracts simulated T using nodes and weights from T-COMP_Weight.f
c
c Read regional MODFLOW files.
c Extracts regional gridding, T, & VCONs.
c Read Factors file -- RegionalNAME_TranFACTORS.txt
c Write output TRAN-Simulated.txt file in the format,
c Nsites !! Number of sites to be read
c AquiferTestNAME 0000000.000 !! site name (A32) & transmissivity (G16.8)
c AquiferTestNAME 0000000.000 !! site name (A32) & transmissivity (G16.8)
c AquiferTestNAME 0000000.000 !! site name (A32) & transmissivity (G16.8)
c
C

## Slide 19: Compare T in DV3
270 transmissivity estimates compared to simulated equivalents in DV3 model
  Estimates are unevenly distributed, Clumpy
    Nevada National Security Site (NNSS),
    Amargosa Desert, &
    Pahrump Valley
T comparisons increased awareness of model contents
Examples from NNSS because more information
50 MILES
Focus on
Nevada National
Security Site

## Slide 20: Areal Extent of Sample Volume
Areal extent proportional to volume pumped, to a point
  Maximum specified, Less queasy
T proportional to pumped volume
  Permeable rocks can yield water,
  Tight rocks cannot yield water
Distribute T with pilot points
  Allows spatial variability
Transmissivity observations
  Site specific, Not mashed
  Variability in sample volumes
10 MILES

## Slide 21: Goodness of Fit
Low-transmissivity
observations
Measured = 600 ft²/d
Simulated = 3 ft²/d
Transmissivity estimates
  Good deal of scatter
  95% confidence ±10x
Mismatch less severe compared to range of T observations
  Measured T spans, 10 orders of magnitude
Sample DVRFS.v2, T not used in calibration
  Marked misfit for low transmissivities, T less than 100 ft²/d

## Slide 22: Transmissivity Sampling
Many T estimates at NNSS
  Investigated big volumes beneath Pahute Mesa & Yucca Flat
  Mysteries remain north of Yucca Mountain
Structures beneath Yucca Flat identified problems with complex volume sampling
Pahute
Mesa
Yucca
Flat
North of
Yucca Mountain

## Slide 23: Compare Correctly
(Modified from Fenelon, et al, 2012)
Strong contrasts in permeability
  Overlying tuffs impermeable
  Carbonate rocks transmissive
Wells registered at water table
  Mapped water table is model top
  Mapping imperfect
Need to correct observation
  Revise model top or,
  Move sample volume
Assign field transmissivity to conceptually same layers for comparison to simulated T
T < 1 ft²/d
MODFLOW Layer
T = 10,000 ft²/d
Tuffs
Carbonate Rocks
BOOM!
BOOM!
BOOM!

## Slide 24: Simple Sample Volume
Assign investigation radii to ranges of pumped volumes
Cut-out fractions, Cookie-cutter style
  Same fractional assignments in each layer
Assign to layers by conceptual model
  e.g., Compare well open to carbonate to layer with carbonate rocks
Layer 1, Confining unit
Layer 2, Carbonate Rocks
Investigation radius
from pumped volume

## Slide 25: Average, Not Geometric Mean
Transmissivity averaged in model layer
Conceptually consistent with interpreting impermeable features
Consider single-well test
  Aquifer has T = 8,000 ft²/d
  Homogeneous aquifer, Results agree
  Half clay, T~ 0 ft²/d, Aquifer-test results half
    NC-GWE-GF-04PB carbonate rock well, T~70,000 ft²/d
    Clay west of Gravity fault; ~¼ mi west of well
  ¾ clay, Aquifer-test results ¼
Sample circle & interpret significance
8,000 ft²/d
Pumping
Well
PLAN
VIEW
0 ft²/d

## Slide 26: Further Interpretation
Apparent conflict exists between T estimates around ER-6-1-2main
  30,000 ft²/d from Cooper-Jacob
  300,000 ft²/d from calibration DV3
High-T in narrow corridor
  Width of 1.5 mi
  Small T in surrounding rocks
Sample larger area
  Expand radius to 10 mi
  Simulated T averages 30,000 ft²/d
Observed drawdowns support big area
(Jackson and Halford, 2019)
Yucca
Flat
15 MILES
ER-6-1-2m
Drawdown
observed
Tracer-3

## Slide 27: Conclusions
Transmissivity most direct synthesis of aquifer-test results
Transmissivity observations
  Better than mashing into broad categories
  Some subjectivity, Better than ignorance
  Rationale and tools available
Specific information improves results
  Low transmissivity important
  Not including weakens results of interest

## Slide 28: End Section