## Slide 1: Aquifer Test Overview

## Slide 2: Purpose
WHY—Can’t stick a flow meter in ground
See responses to flow
  Slug—Connection of well & aquifer
  Pumping—Connection between wells
Estimate representative hydraulic properties
  Transmissivity (T) for all types of analyses
  Storage coefficient (S) if multiple well
  T & S knowable because flow rate (Q) known
Area investigated
  Volume of pumped water

## Slide 3: Test Design
Test design should consider
  Properties of interest
  Representativeness of hydraulic property estimates
    Volume affected— Slug small, Pumping big
      Slug — ½ to 1 gallon
      Single well pumping — 350 gpm, 24 hours ~ 500,000 gallons
  Confirm connection or barrier in aquifer
    Well placement and stress distributions
    More detail requires more wells
      Multi-well pumping — 5,000 gpm, 31 days ~ 223,000,000 gallons ~ 700 acre-ft
Design test around needs, NOT analytical constraints

## Slide 4: Stress & Observe
Pumping or slug creates stress
  Volume of change known
  Steady & clear signal best
Water-level changes are observed
Drawdowns are,
  Differences between observed water levels and what water levels would have been in the absence of pumping
  NOT necessarily change since start of pumping, s = h – h0

## Slide 5: Conceptualization
Release of water from storage
  Rates of release
  Drawdown patterns
Detectable extent of drawdowns
  Volume – Area & thickness investigated
  Discharge
  Elapsed time

## Slide 6: Hydraulic Conductivity (K)
Mr. Darcy’s fudge factor
Accounts for
  Permeability of rock
  Viscosity of water
  Gravity, being on Earth
Minor problems from lumping
Relates flow to head drop
For a given head difference,
  Double K
  Double flow (Q)
K less useful term in practice
(Modified from Heath, 1983)

## Slide 7: Transmissivity (T)
Transmissivity is defined as
  Hydraulic conductivity (K) x Thickness (b)
Thickness not always known
Transmissivity (T)
  Estimated from aquifer tests
  Easy to apply to cross-section
  Easily mapped
T less variable than K x b
  Analogous to weight of passengers on plane
    Weight of individuals & baggage quite variable
    Combined weight of 200 passengers varies less
Surface Trace
Cross Section

## Slide 8: Storage Coefficient (S)
(Heath, 1983)
Unit declines
in heads
Water released from storage
Specific yield—Drainable water
  Long term (years) source
    Basin Fill 10 to 20 percent
    Fractured Rock 1 to 4 percent
Confined— Squishiness of Rock & Water
  Thickness x compressibility, 0.0002 to 0.002
    Compressibility not variable
    Specific storage ~ 2 x 10¯⁶ 1/ft

## Slide 9: Confined Response
Pumped water from rock & water compressibility
Water evolves across full aquifer thickness
Primary contributing area moves away from pumping well
  Bulk of water released from storage at edge of drawdown cone
10
100
1,000
10,000
RADIAL DISTANCE, IN FEET
CONFINING UNIT
Drawdown
Drawdown
Drawdown
QOUT

## Slide 10: Unconfined Response
Compressible storage initially
Water mostly from drainage
  Water evolves from water table
Vertical flow occurs
  Drainage at water table
Horizontal flow to screen
  Vertical anisotropy, Kx/Kz, matters
  Greater vertical anisotropy delays transition to drainage
Cone of depression expands slowly
CONFINING UNIT
10
100
1,000
10,000
RADIAL DISTANCE, IN FEET
Drawdown
Drawdown
Drawdown
QOUT
KX
KZ

## Slide 11: Vertical Anisotropy
Horizontal & vertical usually differ
Alluvial sedimentary structures
  Bedding, Small scale grain orientation
  Clay lenses, Larger scale heterogeneity
Horizontal, KXY, > Vertical, KZ
Vertical anisotropy, KXY:KZ , lumps
  Address ignorance with simple club
  Data frequently not sufficient to define
Increased vertical anisotropy
  Drawdowns propagate further
  Aquifer response approaches Theis
CONFINING UNIT
Bedding
CONFINING UNIT
Clay lenses
CONFINING UNIT
Vertical anisotropy
KX
KZ

## Slide 12: Lateral Anisotropy
Transmissivity assumed isotropic
  Same radial distance, Same drawdown
  Expands uniformly, Circles
  Single well, Must be true
Observation wells reveal asymmetry
Invoke lateral anisotropy
Alter transmissivity tensor
  Unequal magnitudes & rotated
  Easy math for analytical solutions
Data needs limit application
Use heterogeneity instead
TX
TY
QOUT
Plan view
5
2
5

## Slide 13: THEORY

## Slide 14: Simplifying Assumptions
Homogeneous & laterally isotropic
Flow patterns are radial, Reduces 3D to 2D
Infinite extent of aquifer
Thickness of aquifer is uniform
(Heath, 1983)
2D
1D

## Slide 15: More Simplifications
Theis & Thiem solutions— All flow is lateral
  NO vertical gradients – Several conceptualizations
  Reduces from 2D to 1D
  Wells are fully penetrating
Aquifer bounded by impermeable confining units
Ignorance usually restricts more than analytical assumptions
10
100
1,000
10,000
RADIAL DISTANCE, IN FEET
CONFINING UNIT
Drawdown
QOUT
Theis Response
Water released from storage

## Slide 16: Theis—Transient Flow
Theis solution, storage (S) is the only source of water
Additional assumptions:
  No wellbore storage – Line sink
  Water released from storage instantaneously
Drawdown is a function of radial distance, time, T and S

## Slide 17: Theis—Solution
Analytical solutions solved in terms of dimensionless groups
W(u), well function, is an exponential integral solution
Drawdown increased by
  Increasing Q or
  Decreasing T
Drawdown affected equally by
  Radial distance squared, r²
  Storage coefficient, S
  Inverse transmissivity, 1/T
Where,
or

## Slide 18: Type Curves
Theis equation solved in type curve
  Solution plotted log-log
  Drawdowns plotted log-log another sheet
  Fit measured drawdowns to type curve
  s & time at match point define T & S
Type curves
  Great pre-computer
  Pointless after 1990
  Log-log legacy lives on today
Semi-log plots more useful
  Both assessing fit & conceptually
(Berger et al, 2004)

## Slide 19: T & S Effects
High T produces a broad, shallow cone of depression
Low T - deeper, less extensive cone
Unconfined (high S) -- slows growth of cone
Confined -- cone of depression spreads quickly
t = 0
AQUIFER
t = later
AQUIFER
Low T or High S
High T or Low S

## Slide 20: Go to Workbook
File in Example folder
  01_Theis-Distance.xlsm
Use Theis solution
  Plan for tests
  Examine possible responses
  Requires minimal knowledge
Analytical Distance-Drawdown
  https://halfordhydrology.com/analytical-distance-drawdown/

## Slide 21: Volume Pumped
Example, SW Big Springs well, Snake Valley, NV
Pumped 170 gpm for 2 days, V = 500,000 gal.
Return flow not an issue
  355 ft to water & slope below site ~10%
Q = 170 gpm
V = 500,000 gal
Snake &
Hamlin
Valleys

## Slide 22: Area Investigated
SW Big Springs well
  ~ 500,000 gallons
No drawdown Big Springs NW
  Detection limit ~0.02 ft
Volume of rock bigger
  Transmissivity 4,400 ft²/d
  Storage coefficient
    Unconfined ~0.1
    Confined ~0.003
Area investigated ranges from 60 to 2,000 acres
N
Unconfined
Confined
2 MILES
Big Springs SW
Hamlin
Valley
(196)
Snake
Valley
(195)
Big Springs NW

## Slide 23: Superposition

## Slide 24: Additive Effects
Aquifer testing analyzes change from pumping
Groundwater levels measure responses to all stresses
  Natural fluctuations— Barometric, tidal, and recharge forcing
  Drawdowns from pumping
Superposition assumes all effects additive
  Drawdown = Groundwater levels - Natural fluctuations
Superposition also approximate spatial & temporal heterogeneity
  Impermeable boundaries
  Stream capture
  Variable pumping schedules

## Slide 25: Real Divide
Pumping well, Q1, causes drawdown, s1
Pumping well, Q2, causes second drawdown, s2
Total drawdown is sum of drawdowns s1 and s2
Groundwater divide exists between wells
Water enters well 1 from left and well 2 from right
As long as Q1 = Q2, the divide remains
Aquifer
Q1
Q2
s1
s2
DIVIDE

## Slide 26: Image Wells
IMAGINARY
Replace pumping well, Q2, with imaginary well
Pumping from image well always equal to pumping real well
Superposition simulates no-flow boundaries, faults
Real & imaginary wells simulate no-flow boundary
Imaginary injection well simulates a stream, Glover solution
Aquifer
Q1
Q2
s1
s2
DIVIDE
REAL
No-flow

## Slide 27: Superposition in Time
Simulate pumping schedule
Simulate drawdown, s, from each change in flow rate, ΔQ
  Each change starts as time0 in Theis
  Each drawdown simulated forever
For example
  Q increases, 150 to 450 gpm, day 4
  ΔQ = +300 gpm, Δt = time – 4 days
  Drawdown, s = s1 + s2
ΔQ1= 150
s1
ΔQ2 = 300
s2
TIME, IN DAYS | PUMPING, IN GPM | CHANGE, IN GPM
0 | 150 | +150
4 | 450 | +300
10 | 0 | -450

## Slide 28: Superposition in Time
Simulate cessation of pumping
  Inject final pumping rate,
  ΔQ3 = -450 = 0 – 450 gpm,
  Δt = time – 10 days
  Drawdown, s = s1 + s2 + s3
Functions show summed results
Superposition remains useful, even with numerical models
Important for aquifer tests, Assess change
Reilly, et.al., 1987, The principle of superposition and its application in ground-water hydraulics, USGS TWRI03-B6, 28 p. https://doi.org/10.3133/twri03B6
Leake, S.A., 2011, Capture—Rates and Directions of Groundwater Flow Don’t Matter!. Groundwater, 49: 456-458. https://doi.org/10.1111/j.1745-6584.2010.00797.x
ΔQ1= 150
s1
ΔQ2 = 300
s2
ΔQ3 = -450
s3

## Slide 29: End Section