## Slide 1: Slug Test Analysis

## Slide 2: Uses
Local estimate of transmissivity across well screen, K = T/bscreen
  Fair enough, Given small volumes
  Only viable test in tight rocks, K < 0.1 ft/d
Preliminary test for designing larger multi-well aquifer test
Check hydraulic connection between well & aquifer
  Test well development
(Halford and Kuniansky, 2002)
Notes: Multiple slug tests can show that the well is not fully developed.
With older observation wells, these should be checked about every 5 to 10 years to see if the well needs some maintenance or if an old observation well is going to be added to a network after several years of no use.

## Slide 3: Common Place
Low cost and simple
Relatively rapid, Site visit less than 2 hours
  Depth to water less than 100 ft
  K >= 1 ft/d, few slugs within ½ hour
Very useful in tight formations
Minimal water disposal
Multiple slug tests – heterogeneity
Simple to analyze
  Estimate a slope from plotted data
(Halford and Kuniansky, 2002)
Notes: Cost and ease--can be performed by one, at most two people at multiple wells. Just need a transducer, data logger, and different size slugs.
Rapid -- in most formations that are considered aquifers the recovery time can be less than a minute. In less permeable formations can take hours
Tight formations --can’t perform pumping test because of problems maintaining a pumping rate without dewatering the well. Other options are constant head injection test or lab core permeability.
No Water -- Major advantage at hazardous waste sites. The only waste water would be the water used to decontaminate the slug.
Typically done at hazardous waste sites -- run multiple tests at all of the wells in an area
Analysis -- Most analysis involves fitting straight lines or type curves to correctly plotted field data.

## Slide 4: Terminology
Sudden rise in head
  Falling-head test,
  Slug-in test
Sudden drop in head
  Rising-head test,
  Bail-down test,
  Bailer test,
  Slug-out test,
  Withdrawal test
Rise in head
Drop in head
Notes: Just to clarify that many people like to distinguish between the two types of tests. This is critical for unconfined aquifers where the water level is below the top of the screen--ONLY the slug-out or rising-head test should be analyzed.

## Slide 5: Slug-Test Review
Rapid addition or removal of a known volume from well
  Stresses the aquifer
Transmissivity or K*bSCREEN
  Inversely proportional to recovery rate
  Specific solutions provide different well & geometry corrections
TIME

## Slide 6: The Slug
Known volume
  Displacement length (h0) times
  Casing area, pdc2/4
Slug wells with,
  Weighted rod, Filled pipe
  Pressurized air
  Jug of water
Check basics
  3.3-ft x 1½-in rod = 0.3 gal
  h0 ~ 2 ft, 2-in casing
K
KA
h0
H
D
dc
dA
L
Diameter, inches | Gallons per foot
2 | 0.16
6 | 1.47
12 | 5.88
24 | 23.50
Abbreviation | Term | Unit
K | Hydraulic conductivity of aquifer | L/T
KA | Hydraulic conductivity of gravel pack | L/T
dC | Diameter of casing | L
dA | Diameter of wellbore | L
h0 | Initial displacement | L
L | Length of screen | L
H | Water table to bottom of screen | L
D | Aquifer thickness | L

## Slide 7: Known Flow Rate
Measure change in head
Flow to well is
Q = -prc2 dy/dt
Q little fuzzier where water table in well screen
  Minor error relative to method
Known Q allows estimation of
  Transmissivity or
  K*bSCREEN
dy / dt
h0

## Slide 8: Thiem Type Analyses
Flow from aquifer defined with Thiem eq.
  Hvorslev (1951), analytical shape factors (Sf) for assumed flow — spherical, cone, etc.
  Bouwer and Rice (1976), Outer radius, Re , empirically derived
  Solidify proportionality with fudge factors
No drawdown at empirically derived Re
  Conceptually difficult – Transient event
  Pragmatically works – Known error minor
    Order of magnitude estimates
    Volume investigated typically small
Shape
Factor
Slope of
Response

## Slide 9: Bouwer & Rice
Empirical shape factors developed with an electrical analog model
Higher conductivity KA assumed for annular fill, Relative to hydraulic conductivity of aquifer, K
Ceases to matter where untrue, K > KESTIMABLE
DrC2 ln(Re/rA)
ln(y2/y1)
t2 - t1
2L
K =
Shape
Factor
Slope of
Response
h0
dc
dA
K
KA
H
D
L
(Bouwer and Rice, 1976)

## Slide 10: Empirical Estimate of Re
All coefficients defined by ratio of screen length to annular radius
Coefficients
  A & B for partial penetration
  C for fully penetrating screen
Results minimally affected by finely tuned fudge factors
ln =
Re
rA
1.1
A + B ln[(D-H)/rA]
L/ rA
ln(H/rA)
+
[
]-1
Partially penetrating
ln =
Re
rA
1.1
ln(H/rA)
C
L/ rA
+
[
]-1
Fully penetrating

## Slide 11: Transient Analyses
Slug test does create transient response
Cooper et al (1967) developed type curves for Theis aquifer
  1-Dimensional
  T & S define response, h/hₒ
Greene and Shapiro (1998) modified for prematurely terminated slug tests
  Air-pressurization is the slug
Storage not estimable
  Examples with 2-in. well
    Slope only information
    Minimally changed by storage coefficient
t = 6 sec T = 10 ft²/d
t = 1 sec T = 60 ft²/d

## Slide 12: Avoidable Errors
Wells screened across water table usual culprits
  Use wetted screen not screen length
  Adding water complicates results by increasing wetted length
  Use correct well construction
    Reported water level above well bottom
    Diameter of casing smaller than annulus
Apparent competence affected more than transmissivity estimate
Leaky slug
Wetted screen
Bad construction

## Slide 13: Slug-Test Workbook
Slug_KGS-BnR-2019.v3.xlsm, Combines tools
  Bouwer & Rice from (Halford & Kuniansky, 2002)
  KGS solution (Butler, et al, 2003)
Added tools
  Display full time series
  Select displacements to analyze
  Manually adjust start & displacement of each slug
  Regress or manually fit data
Simplified input & output

## Slide 14: Chicago Valley
Chicago Valley
  Pahrump Valley (HA 162) upgradient
  Lower Amargosa river downgradient
Wells drilled
  Characterize rocks at depth
  Estimate hydraulic properties
CHV1 shallow – 620–640 ft
CHV1 deep – 880–890 ft
150 MILES
N
Chicago Valley wells
NEVADA
UTAH
CALIFORNIA
NEVADA
Extent DV3 model
CHV1 shallow
CHV1 deep

## Slide 15: Chicago Valley deep
Chicago Valley deep
  Measure water above transducer
  Introduce slug, Wait awhile
  Slugs 2 & 3 synthetic with added noise
Formation tight
  Recovery ~ an hour, 45 min. window
  T = 2 ft²/d, K = 0.1 ft/d
  Reasonable for siltstone
T or K  slope
  T = 20 ft²/d, 4.5 minutes
  T = 180 ft²/d, 30 seconds
  T > 1,000 ft²/d, 5 seconds
T = 20 feet²/day
Measurement limit

## Slide 16: Chicago Valley shallow
Chicago Valley shallow
  Water level measured every 0.3 second
  Introduce slug, Wait awhile
  Remove & insert slug every minute
  Oscillating or underdamped response
Displacement, y0, should not vary
  Single slug with fixed volume
  Withdrawal close enough
  Insertion problematic
    Jump 1st second, likely shock
    y0, estimated without jump
Oscillating response decays ~3 min.
Withdrawal
Insertion
Ain’t Right

## Slide 17: Oscillating or Underdamped
Inertia of water column > friction
  Transmissive formation, less friction
  Long water column, more mass
Solutions couple
  Momentum in well
  Radial flow in aquifer
van der Kamp (1976) solution
  Reflect about initial water level
  Slope defines K*bSCREEN
KGS solution (Butler & Garnett, 2000)
  Solves underdamped problem
  Smoothly transitions to overdamped
Overshoot from momentum

## Slide 18: Analysis of CHV1 site
CHV1 shallow,
  Not super transmissive
Underdamped response
  Transmissive enough &
  Long water column
Example problem
Well | CHV1 deep | CHV1 shallow | 
LCOLUMN | 700.0 | 500.0 | ft
y0 DISPLACEMENT | 1.5 | 1.7 | ft
K * bSCREEN | 2.0 | 700.0 | ft²/d

## Slide 19: Class Example