## Slide 1: Single-Well Pumping Analysis

## Slide 2: Single-Well Pumping
Estimate transmissivity opportunistically
  Only 1 well needed
  Pumped well unambiguously “sees” pumping rate
  Simple drawdown, s, estimate adequate
    Change from pre-pumping water level, s = h – h0
Relatively independent of well construction
  Inefficient wells increase uncertainty
  Magnifies response to small changes in flow rate
Simple analysis
  Fit a straight line

## Slide 3: Cooper-Jacob
Theis equation,
W(u) complex part of solution
  u, dimensionless time,
Solved with series expansion,
Drawdown (s)  ln(u), u < 0.1
  Less than 2 minutes in extreme
  Typically within seconds
Semi-log, straight line OK answer
For u < 0.1
W(u) = -0.5772 – ln(u)

## Slide 4: Cooper-Jacob Analysis
Simplify by differencing 2 points,
  Differenced equations,
  Rearrange for convenience
Estimate transmissivity (T)
  Determine discharge & slope, Δs
  Estimate drawdown & plot semi-log
  Eyeball slope, visually filter trash
&
Common log
for
hydrologists
&
DRAWDOWN
h0
t1, s1
t2, s2

## Slide 5: Half Moon Lake, FL
Apply to 1-day test in Tampa
  Pumping rate 790 gpm
  Simple estimation of drawdown
  Plot semi-log, Elapsed time & drawdown
  Eyeball slope with a line
  Defines pair of points
  Reduce to slope per log-cycle, Δs
  Estimate T with slope, Δs, estimate
DRAWDOWN
0.01, 12.93
1.0, 15.01
(Metz and Sacks, 2002)

## Slide 6: Storage Coefficient—BAD
Storage coefficient, S
  Can be estimated
  Cannot be trusted
Estimate time, t0, when s = 0
Estimate S at Half Moon Lake
  S = 0.001 is reasonable, not
Skin & partial penetration
  Increases drawdown
  Shifts time intercept
  S grossly underestimated
days
= =

## Slide 7: Transmissivity—GOOD
Transmissivity  slope
Estimate slope,
  Ideal well, No head losses
    Horizontal flow in aquifer
    No well entry losses
  Real well, Head losses
    Converging flow in aquifer to Partially penetrating well
    Plugging in gravel pack & screen, Skin aggregate term
Drawdown offset, slope same
Ignore first 10 minutes
  Negates wellbore storage & well loss
KBASIN FILL
KCARBONATE
CONFINING UNIT
SKIN
Slope

## Slide 8: Cooper-Jacob Recovery
Time since pumping started
Time since pumping stopped
Model uses superposition in time
  Elapsed time from pump on, t + Δt
  Elapsed time from pump off, Δt
Production well, usually
  u is small, < 0.01, so s proportional ln(u)
  Straight-line works
Manipulate time for semi-log straight line
  Time started / Time stopped
  Latest data approach 1
  Δs same as in,
Average flow good enough
Q
+
-
(t+Δt)
Δt
T = 5,000 ft²/d
Meaningless units
TIME
Early
recovery
Late
recovery

## Slide 9: WW- A (1870 ft)
Water supply well
  USGS 370142116021101 159 S10 E53 26 1 WW- A (1870 ft)
  Basin fill above tuff pile, Yucca Flat
  Variable flow rates,
  850 million gallons, 1960 to 1988
Recovery water levels
  1994 to 2015
  Observed rise > 5 ft, Bigger than noise
  Explains changes well
Opportunistic estimate
  Sampled large volume
  Pretty certain T ~ 200 ft²/d
  Big average, 3-4 mile diameter
T = 110 feet²/day
T = 230 feet²/day
Pumped from 1960 to 1988 Q = 60 gpm
T = 180 feet²/day

## Slide 10: Cooper-Jacob Workbook
ª Cooper and Jacob (1953), free copy
CJ-Drawdown+Recovery.v5.xlsm, Combines tools
  Cooper-Jacob (1946)ª pumping
  Cooper-Jacob (1963) recovery
  Both (Halford & Kuniansky, 2002)
Added tools
  Display time series
    Differentiate drawdown & recovery
    Identify analyzed data points
    Highlight pumping
  Regress or manually fit data
Simplified input & output

## Slide 11: Combine Drawdown & Recovery
Measured semi-log slopes same, Drawdown (DD) & Recovery (Rec)
2 curves plot different space
  Rec time, (t+Δt)/Δt, altered from days
  Drawdowns greater than recoveries because of well losses when pumping
Align recovery with drawdown
  Shift Rec time by multiplying,
    last DD time / first Rec time
  Shift recovery to drawdown by adding,
    1st analyzed drawdown
  Add reminder of transforms
Slope = 3.7 Feet/log-cycle
Multiply (t+Δt)/Δt by 0.004
Add 1st analyzed drawdown, 21 ft
Recovery curve shifted by,
Δt-Qstart/Δt-Qstop divided by 481
21 feet were added to residual drawdowns.

## Slide 12: Example

## Slide 13: Jacob-Lohman
Analyze flowing wells
  Constant drawdown, h0, before opening
  Open well, Measure decline in Q
  Estimate slope, s/Q, Note transform
Theis aquifer assumptions
  Radial confined flow, Infinite extent, fully-penetrating well, etc.
Analyze semi-log, time – s/Q
  Bigger values, s/Q, Smaller Q
Not needed for shutting-in well
  Cooper-Jacob recovery works
  Measure pressure build-up
(Jacob-Lohman, 1952)

## Slide 14: Jacob-Lohman Workbook
JL-DecliningFlow-2019.xlsm
  Revised from, Halford & Kuniansky, (2002)
Added tools, again
  Display time series
  Identify analyzed data points
  Regress or manually fit data
Simplified input & output
Infrequently used
Apply to tunnels
  Rotate well 90°
  Minimal boundary effects, Low-K rocks
(Jacob-Lohman, 1952)

## Slide 15: Rainier Mesa, NV
Detonated nuclear devices in tunnels beneath Rainier Mesa, NTS
Tunnels overcome technical limits
  Measure emitted particles
  Irradiate experiment but Plug tunnel before debris hits
  Experiment tunnels ~½ mile long
Tunnels are not small features
  100 in. emplacement holes look petite
61 nuclear tests & decades later, Where are the radionuclides now?
  Need hydraulic conductivity to answer
(Wilborn, 2018)
(Drollinger, et al, 2009)
(Diamond Sculls, T-tunnels)

## Slide 16: U -12e Tunnel
Rainer Mesa recharge area
  Straddles 3 groundwater basins
Tunnels mined into Rainier Mesa
  Volcanic tuffs, Low-K rocks
  Above regional water table
  Little water drains from tunnels, Except when wet, blind faults mined
E-Tunnel first mined
  20 years of active mining & testing
  About 46,000 ft or ~9 miles cumulatively mined
(Wilborn, 2018)
E-Tunnel

## Slide 17: Low-K Estimates
E-Tunnel drainage measured
  Consistently after 1996
  Long-term decline, Draining tuffs
  Flow spikes, Fracture flow
Pre-mining water levels speculative
  360 ft above floor best estimate
  200 ft above floor lower bound
  K increases as drawdown decreases
Bulk estimate K = 3 x 10-5 ft/d
  K does not exceed 1 x 10-4 ft/d
  Same results from prolonged numerical analysis
Drainage
Wet
Winters

## Slide 18: End Section