## Slide 1: Multiple-Well Tests & Drawdown Detection

## Slide 2: Multiple-Well Aquifer Tests
Hydraulic properties other than transmissivity can be estimated
  Specific yield – More variable in hard rock, 0.5 to 2%
  Hydraulic conductivity of confining unit
  Heterogeneous hydraulic conductivities
Observing responses to pumping, More important (usually)
  Proving hydraulic connections
    Exist – Definitive result if observed
    Precluded – Ambiguous result, Sensitive to drawdown detection threshold
  Capturing spring flow, Same happens or doesn’t results
    Measuring changes in flow more uncertain than changes in water levels

## Slide 3: C-AQUIFER EXAMPLE

## Slide 4: C-Aquifer, Arizona
C-aquifer evaluated as alternative water supply
Multiple-well aquifer test
Results interpreted with multiple methods
  Specific capacity
  Distance drawdown
  Cooper Jacob
  Numerical model
Kept estimating T during test
  Continually refine estimates
(Hoffmann and others, 2005)
5 MILES
N

## Slide 5: Site #3 Pumping Well
Pumping well for site 3, PW3
  Depth to water level, 225 ft below land surface
  Maximum pumping rate 800 gpm
Discharge conveyed 500 ft to dry channel
  Water discharged away from pumping & observation wells
  Avoid return flow & complicating recharge signal
Pumping Well #3
Discharge line

## Slide 6: Measuring Discharge
Flow measured with
  Inline flowmeter primarily
  Manometer secondary method
Flow also estimable from
  Vertical drop &
  Horizontal displacement
3.23 ft
0.47 ft

## Slide 7: Observation Wells
Radial distances
  A-wells, 180 ft
  C-wells, 290 ft
  Windmill, 530 ft
Observation well depths
  Water table, A2, C3, & 5M-88
  Pumped interval, A1 & C2
  Deepest, C1 at 1,160 ft BLS
Four major units
Piezometers A1 & A2
Coconino
Sandstone
Schnebly Hill
formation
Coconino & Schnebly Hill
Supai Formation

## Slide 8: Responses to Pumping
Most drawdown in pumping well occurs within hours
Shallow piezometers respond less, water-table
Deeper piezometers respond more, confinement
Empirically estimate T from SC
  Specific capacity, SC = 2.4 gpm/ft
  T, ft²/d = 230*SC, gpm/ft (Thomasson, et al, 1960)
  T, ft²/d = 380*SC, gpm/ft (Frus and Halford, 2018)
  T < 1,000 ft²/d
Test 1
750 gpm
Test 2
750
gpm

## Slide 9: Cooper-Jacob
Analyze pumping well during test 2
T = 10,000 ft²/d
  Good initial estimate
  Lot of drawdown in pumping well
Well efficiency <10%
  Less than ideal screened interval
  Screened in tighter rocks
Minimally affects Cooper-Jacob
  Analyze slope
  All flow affects water levels
Slope = 2.7 Feet/log-cycle

## Slide 10: Drawdown, Site 3—Test #2
Water table wells
  Drawdowns 2-3 ft
  WW5M-88 further than C3, but deeper
Pumping interval
  Expected distance-drawdown response
  Unconfined aquifer response
  Fluctuating discharge observed, Variable viscosity in discharge line
Deep well, C1-Obs, anomalous
  Lagged in time, but greater drawdown
  Poor communication with aquifer
  Aquifer is not homogeneous
Slope ~1.8 feet/log-cycle

## Slide 11: Distance-Drawdown
Plot semi-log distance-drawdown
  Estimate slope & estimate
  Transmissivity & specific yield
  Workbook for Distance-drawdown
Properties for site 3
  Transmissivity ~ 3,000 ft²/d
  Specific yield ~ 0.05
Expensive method, Adds little
  Single-well analysis more reliable
Water Table wells

## Slide 12: Geologic Column in MODFLOW
Analyze heterogeneous aquifers
  Define 4 geohydrologic units
Production well & aquifer simulated
  Simulates wellbore storage
Axisymmetric, radial geometry
Solved with MODFLOW
Estimate hydraulic properties
  Kx of 4 geohydrologic units
  Vertical anisotropy
  Specific yield
  Specific storage
Coconino sandstone with minor Schnebly Hill near base
Schnebly Hill formation
Coconino SS and Schnebly Hill
Supai Formation

## Slide 13: MODFLOW Comparison
Simultaneously simulate & explain both pumping & recovery periods
Measured & simulated drawdowns agree, RMS error = 1.5 ft
Lateral heterogeneity likely exists
  Wrong pattern in pumping interval, Wells A1-Obs & C2-Obs
  Mismatches in water table wells
  Pattern error & noise similar magnitude
Accept errors for generalized result

## Slide 14: Drawdown Section,1-Day
Could detect drawdowns greater than ½ mile from pumping well
Pump 70% of 750 gpm from 10% of screen
Schnebly Hill Formation
Supai Formation
500 FEET
Drawdown, in feet
0.01
0.1
1
10
100
Depth below land surface, in feet
500
1,000
1,500
Coconino Sandstone
5M
-
88
A2
-
Obs
C3
-
Obs
A1
-
Obs
C1
-
Obs
C2
-
Obs
PW3

## Slide 15: Hydraulic Properties
Upper 500 ft contains >95% of transmissivity
Vertical-to-horizontal anisotropy is 0.2
Specific Yield is 5%
Small specific storages suggest fracture flow

## Slide 16: SUMMARY, Site 3
Very low efficiency of pumping well
  Pumped interval not transmissive
  Coconino Sandstone 20X greater permeability than Schnebly Hill formation
  Specific capacity underestimated T because low efficiency
Cooper-Jacob and distance-drawdown bracket numerical results
  Analytical between 3,000 and 9,000 ft2/d
  Numerical ~ 6,000 ft2/d
Illustrates preserving transmissivity
(Hoffmann and others, 2005)

## Slide 17: Drawdown Detection

## Slide 18: Other Signals
40 MILES
Wells WW-4a & WW-4 supply wells in CP basin, NNSS
  WW-4a primary supply well
  WW-4 observation well
  1,200 ft between wells
Aquifer test of opportunity
  Pumping rate 620 gpm
  Schedule measured
  Monitor water levels in both wells
  Analyze longer duration pumping cycle
Response very interesting, Clearly dual-porosity
https://nevada.usgs.gov/aquifertests/studies/tests.html?test_pg=ww4a
3,000 FEET
1200 FT
N
Dual-porosity response

## Slide 19: Dual-Porosity
Water released instantly in Theis
Dual porosity delays release
  Fractures —Theis solution
  Matrix—1D Linear / Spherical, Boundaries, sFRACTURE & No-flow
Analytically feasible, kind-a sort-a
Response similar to drainage from water table in unconfined aquifer
Conceptual arguments more important than solutions
Attracts needless publishing
  Evaluation of Quintuple Porosity in Shale Petroleum Reservoirs
https://nevada.usgs.gov/aquifertests/studies/tests.html?test_pg=nts_singlewell_UE-19fs

## Slide 20: Noise & Interpretation
WW-4a supply well, Keeps filling tank
Repeat pumping, Repeat responses
Interesting responses unrepeatable
  Dual-porosity response,
  Unconfined drainage,
  Other stresses look alike
Earth tides & barometric effects bulk of “interesting” responses
Monitor much more than pumping period for appropriate context
http://nevada.usgs.gov/water/AquiferTests/ww4a.cfm?studyname=ww4a

## Slide 21: Ageless Problem
Measured water levels sum
  Drawdown &
  Environmental fluctuations
Estimate water levels had pumping not occurred
Limited corrections
  Extrapolate trend
  Background well close
Ignore short-period “noise”
(Halford, 1997)
(Stallman, 1971)

## Slide 22: Drawdown Detection
Estimate drawdown
  Great distance
  Adjacent aquifers
  High transmissivity
Detecting small changes difficult
  Environmental fluctuations mask drawdowns less than 0.3 ft
Requires water-level modeling
  Estimate water levels in well if pumping had not occurred
PUMPING
PERIODS

## Slide 23: Water-Level Modeling
Sum possible sources
Natural signals
  Tides
  Barometer
  Background water levels
Natural components can be correlated
Pumping
  Superimpose Theis
  Transform function
  T & S limited to no value
Theis Transform
Synthetic water levels

## Slide 24: Synthetic Water Levels
is an offset, L
n is the number of time series components
is the time series component
is the amplitude multiplier of the ith component, L
is the phase shift of the ith component, T
is the value of the ith component at time
All series interpolated ► Functions are smooth
Estimated
(Halford and others, 2012)

## Slide 25: Water-Level Modeling
Fit measured water levels
Adjust amplitude and phase each series
Drawdown = Theis Transform - Residuals
-0.5
0.0
0.5
1.0
1.5
04/08
04/15
04/22
04/29
05/06
05/13
05/20
05/27
06/03
06/10
WATER LEVEL CHANGE, IN FEET
Theis Transform
Pumping
EarthTide
GravityTide
Barometer
Barometer Avg 1d
Barometer Avg 7d
Background
Background Avg 1d
Synthetic
Measured
Drawdown

## Slide 26: Wah Wah Valley, Utah
Groundwater development Western Utah
  Similar to SNWA project
Estimate hydraulic properties
  Transmissivity &
  Storage coefficient
Use existing wells in Wah Wah
  Wells far apart, greater than 1 mile
Pump a lot to have a chance
  1,200 gpm, 7 days
  > 12 million gallons, < 40 acre-feet
2 MILES
7800 FEET
(Gardner and others, 2020)
N

## Slide 27: Mostly Monitoring
Ample monitoring makes results possible
Maximum drawdown, 1 week after pumping ceases
Pumping period small relative to required record
  Small drawdown plausibly estimated because of antecedent fit
Peak Displacement

## Slide 28: Pahute Mesa, NNSS
Delineate & predict tritium plume
  Define hydraulic conductivity distribution
  Dozens of new wells
  16 pumping aquifer tests, Most multiple well
ER-EC-13 aquifer tests
  Upper zone, 8 million gallons
  Lower zone, 6 million gallons
Observation wells > 1 mile away
  Drawdowns detected 5 other sites
  2-3 miles from pumping well
ER-EC-13
Upper &
Lower
6 MILES
(Garcia and others, 2017)
N

## Slide 29: Expanded Volume
Response replicated between wells ER-EC-13 & ER-EC-1
  Upper zone, UZ test, Summer 2012
  Lower zone, LZ test, Spring 2013
  Packer between UZ & LZ failed
  Same intervals pumped both tests
Maximum drawdown
  ~1 inch
High confidence in results
  Repetition with 2 tests
  Antecedent & recovery data, lots
https://nevada.usgs.gov/aquifertests/studies/tests.html?test_pg=Pahute_Mesa_16

## Slide 30: Long Canyon, NV
Estimate effects of mine dewatering
  Define drawdown extent & connections
    Within Pequop Mountains
    Johnson Springs wetland
    Independence Valley
Define & quantify distributions of
  Transmissivity &
  Specific yield of hard rock
    Variations between 0.5% & 1.5% significant
Variation of K with depth important
  Dewatering rates affected
(Garcia and others, 2021)

## Slide 31: Drawdowns
Pumped 2 wells during 2016
  1,100 & 2,700 gpm
  Cumulative 33 days, 140 million gallons
Continuous monitoring
  118 wells & piezometers
  10 springs
Drawdown detected
  16 wells & 20 piezometers
Capture detected 5 springs
Signals observed 3 miles away
Low resolution devices, ~0.3 ft, Compromise distant detection
Drawdown
Drawdown
Device resolution
Detected
Detected
Ambiguous
NOT detected

## Slide 32: Water-Level Rise
40% of pumpage returns,
  Unintended leakage
Very focused, impromptu seepage runs
Injection approximates, Short reach
Bad, Adds ambiguity
  T & S less unique
  Leakage rate & location known poorly
Good, Identifies
  Transmissive basin fill
  Tight horizons in basin fill
Analyze regardless

## Slide 33: Expected & Investigated Volumes
Original plan for 2016
  7,000 gpm, 1 well
Pumped total 140 million gallons
  2 wells, Odd schedule
Theis approximation with
  Q = 3,200 gpm, 1 well
  t = 30 days
Investigated volume differs
  Many observations to match
  Defines heterogeneity
  Return flow also alters plans
N
3 MILES
EXPLANATION
greater than 0.3 ft of drawdown
greater than 0.3 ft
of water-level rise
observation well
Goshute
Valley
Independence
Valley
2016 test

## Slide 34: Data Changes Concepts
Southern boundary wish driven
  Notable absence of wells
Additional wells for 2018 test
  5 miles south of pumping wells
  Southernmost to confirm barrier
2018 test lasts 74 days
  Q = 4,100 gpm, 440 million gallons
  Drawdown >6 ft in LCP-66A
  Southern boundary further south
Western, northern, & eastern boundaries confirmed by testing
Assumed barrier
2016 test
3 MILES
N
EXPLANATION
greater than 0.3 ft of drawdown
greater than 0.3 ft
of water-level rise
observation well
Independence
Valley
Goshute
Valley
LCP-66A
(Garcia and others, 2021)
2016 test with knowledge
of 2018 responses

## Slide 35: Conclusions
Drawdown detection limit can be reduced from ~0.3 ft to <0.03 ft
  Requires more water-level monitoring
    Background wells monitored in addition to observation wells
    Monitoring includes antecedent and post-pumping periods greater than pumping period
  Measurement resolution of <0.01 ft needed
    Standpipe wells with 5 psi transducers work
    Grouted piezometers less convincing where no signal present
Volume investigated increases >10 times
  Better chance of demonstrating connections or confirming barriers
    Detecting distant signals illustrates connections
    Maximum hydraulic conductance of barrier proportional to drawdown detection limit
      Smaller detection limit reduces potential conductance of barrier

## Slide 36: End Section