## Slide 1: Simple tools for common hydrology problems
2025 NWRA webinar
Tuesday, November 4, 2025

## Slide 2: Common Problems
Review three basic hydrologic problems
  Estimate local flow directions from a few measured groundwater levels
  Refine flow-path interpretation by plotting & mapping water-quality changes
  Graphically estimate & project slopes of water-level changes in a well
Analyze examples of each problem with workbook tools
  KML_3Point-Flow — Estimate flow directions in Amargosa Desert (HA 230)
  Piper & Stiff — Interpret flow paths through Pine & Wah Wah Valleys, Utah
  Slope Finder TOOL — Project water-level changes in a dewatering well

## Slide 3: Local Flow Direction
Solve 3-point problem
  Identify highest & lowest water levels
  Trace construction line between wells
  Middle water level interpolated on construction line
  Draw line of equal water level from middle well to construction line
  Add parallel contours
Defined potentiometric surface with a plane
2 MILES
N

## Slide 4: Fitting a Plane
Define plane with more than 3 wells
  Simulate water level with equation,
  Estimate coefficients a, b, & c
  Minimize weighted, sum-of-squares, SS
    Residuals = measured – simulated
  Measured & simulated water levels differ
    Some measured > simulated
    Some measured < simulated
    Weighted residuals average zero
Process executed in a workbook
N
N
N
N
2 MILES

## Slide 5: KML_3Point-Flow
2 MILES
KML_3Point-Flow.v4.xlsm, estimates plane from water levels
User supplies for each well
  Name, easting, northing, & water level
Refresh button
  Minimizes weighted SS
  Recalculates contours for plane
Evaluate fit with scatter plot
Either adjust weight or remove wells
Evaluate flow direction and contours with map chart
Write KML with “Write KML” button

## Slide 6: Example 3-Point-Flow
Flank of Greenwater Range is example in distribution file
Analyze springs in Ash Meadows
  Near Devils Hole
  Potentiometric surface of full data set not a plane
  Trim observations to what works
Go to subfolder .\KML_3Point-Flow.v4
5 MILES
N
Greenwater Range
Ash
Meadows
Devils
Hole