## Slide 1: Simple tools for common hydrology problems
2025 NWRA webinar
Tuesday, November 4, 2025

## Slide 2
Major-ion Water Chemistry
Piper Diagram (Trilinear Plot)
Stiff Diagram
(Halford & Jackson, 2020)

## Slide 3: Pine & Wah Wah Valleys, Utah
Undeveloped basins in western Utah
Being developed for groundwater export
  Similar to SNWA project in eastern Nevada
Effective sustainable yield estimate
  28,000 acre-ft, Maxey-Eakin (Stephens, 1974 & 1976)
Unique – closed basins at surface however,
  no internal discharge (except for mountain springs)
  Maxey-Eakin estimate not constrained
Groundwater chemistry used in update
  Evaluate the hydrologic connection between foothill springs & valley alluvial aquifers
(Gardner and others, 2020)
Pine Valley
Wah Wah Valley
Snake Valley
Hamlin Valley

## Slide 4: Piper & Stiff TOOL
Major-ion chemistry of groundwater
  used to evaluate groundwater source areas and connection of flow paths in Pine and Wah Wah Valleys
Facilitated with Excel tool
  PiperStiff-QW-2019.v10.xlsm
  Macro enabled
  Very quick and easy to use
  Generates useful, sharable .kmz files
  Generates some figures for publication
Chart: 
Chart: 
Y | 0.1 | 1.1 | 2.101 | 0.1 | 1.1 | 2.101
Y-Log | -3 | -3 | -3 | -3 | -3 | -3 | -3 | -3 | -3 | -3 | -3 | -3 | -3

## Slide 5: Demonstration – Data Worksheet
Required Data:
Lat / Long,
Group,
Site ID,
Major Ion concentrations, in mg/L
Calculated Information:
Estimate of Dissolved Solids,
Charge Balance (using milliequivalent conversion)
Calculated Information:
Meq/L concentrations (initially hidden)

## Slide 6: Demonstration – Piper Worksheet
Piper Plot:
Samples symbolized by grouping
Stiff Figure:
Select site from drop down menu
Figure in upper right
Details in Upper Left
Specific site highlighted on Piper Plot
Generate diagnostic stiff plots,
Generate kmz of stiff plots & view in Google Earth (unhide CONTROL worksheet)