## Slide 1: Simple tools for common hydrology problems
2025 NWRA webinar
Tuesday, November 4, 2025

## Slide 2: Water-Level Change
Estimate rate of change, slope
  Eyeball approach
    Draw a line,
    Move to read rise & run from axes
    Slope = 500 ft / 4 yr / 365 d/yr = 0.34 ft/d
  Add trendline
    Trendline location less than ideal, Slope kind of okay
    2nd trendline not helpful at all
  Create cleverly weighting scheme
    Not fast, Not easy
  Add line segments to define slopes
y = +0.2003x – 7588.9
y = -0.1694x – 8244.3

## Slide 3: Add Line Segments
Create line segments
  Line segment defined with 2 XY pairs
  Slope in 3rd column (I),
  Create multiple line segments to estimate multiple slopes
    Leave blanks between Y values
    Added to chart with single series
Add to chart as new series
Add custom data label for slope

## Slide 4: Slope Finder TOOL
Defined slopes with line segments
  Need to fit segments
  Requires free movement of lines
Facilitated with Excel tool,
  SlopeFinderTOOL.v2.xlsm
  Macro GraphicalSlopeSET
  Operates on other workbooks
Call macro GraphicalSlopeSET
  Alt+F8 or macro button on Developer tab
  Assign macro to QAT (Quick Access Toolbar)
    Step-by-step instructions on Ablebits.com
    How to add a macro button to Quick Access Toolbar
Macro assigned to QAT works best

## Slide 5: Add macro to QAT
Frequent commands assigned to QAT
  Usually assign Excel commands
  Macros also can be assigned
Add tool to QAT
  Rightmost command,
  Select “More commands”
  Select Macros in Excel options
  Add GraphicalSlopeSET to QAT tools
  Select a more representative icon for tool
  Finish with tool in QAT
Tool remains available
  Other workbook selected
  Workbook with tool can be closed

## Slide 6: Example Slope Fitting
Repeat steps in presentation
  Create line segments & slope eq.
  Add line segments to chart
  Add dynamic data label
Open SlopeFinderTOOL.v2.xlsm
  Call macro directly
  Add to QAT table in Excel
Go to subfolder .\SlopeFinderTOOL.v2