## Slide 1: Obtaining Useful Answers from Groundwater Models: INTRODUCTION
Tracie R Jackson, Henderson, NV
Keith J Halford, Carson City, NV
Notes: GM! This workshop is an introduction to GW modeling, where Keith and I will present basin concepts and guidance on how to determine if a model is "good" or "bad" to help you assess whether model results can be trusted.

## Slide 2: Groundwater Models
Simplified representation of a physical groundwater system
Level of detail depends on model purpose
Purpose of model should not be to “build a model”

## Slide 3: Water Supply Questions
What will drawdowns be?
When and where will wells go dry?

## Slide 4: Contaminant Transport Questions
Will release of a solvent pose an environmental risk?
  What is the contaminant source?
  Which way are contaminants moving?
  How soon until a receptor is affected?
  What concentrations are expected at a receptor?
Remediation approach:
  Active or passive water treatment
  Long-term monitoring of wells, springs/streams

## Slide 5: Dewatering Questions
How to optimize mine dewatering?
  Predevelopment/pre-mining water table
  Cumulative dewatering volume
  Maximum pumping rate
  Location/number of dewatering wells
How will groundwater and surface water resources be affected during and after mining?
  Maximum drawdown extent
  Changes in streamflow from mining
  Characterize potential pit lakes
    Recovered stage
    Water budget

## Slide 6: Numerical Groundwater Model Process
Joseph et al. (2016)
Conceptual Model
Mathematical Model
Numerical Model
Harbaugh (2005)
Reality
Abstraction
Representation
Simulation
Notes: Runtime of 1 hour or less

## Slide 7: How is a Groundwater Model Developed?
Compare with field data
Determine historic effects
Understand groundwater system
Define model objectives
Data compilation & analysis
Field data
Conceptual model
Model design
Calibration
Steady state
Transient
Answer Questions
Forecast future effects
Reporting
Grid
Initial conditions
Boundary conditions

## Slide 8: Conceptual Model
Descriptive or graphical representation of hydrologic system
Key components:
  Geologic units and stratigraphy
    Hydrogeologic framework
  Hydraulic properties of geologic units
  Basin setting
    Climate
    Hydrologic boundaries
    Model purpose defines domain extent**
  Water budget
    Recharge
    Natural discharge (springs / streams / ET)
    Pumping / injection wells
  Groundwater-flow paths
  Water chemistry
Joseph et al. (2016)

## Slide 9: Boundary Conditions
Boundary conditions represent interaction of model domain with environment
Three types:
  Type I: Specified head (Constant head)
  Type II: Specified flux
  Type III: Head-dependent flux

## Slide 10: Specified (Constant) Head Boundary
Water body where head elevation is fixed or known with time
At least one location in model must have a specified head to constrain heads
Examples:
  Large reservoir or lake
  Desert playa
    Head is at or near land surface
    Assign head to land surface
    Evaporation rate immeasurably small
    Playas are salt and clay
      Assign low K ~ 10-5 ft/d, which limits flux from playa
Death Valley Playa, CA
(Jackson, et al, 2018)

## Slide 11: Specified (Constant) Head Boundary
Specified head = infinite source of water
Watch for interactions with pumping wells or recharge
Monitor discharges from specified head boundaries to ensure flow rates are reasonable
Specified head
Q
Specified head
Q
Improper placement of specified head?

## Slide 12: Specified Flux Boundary
Discharge is fixed or known with time
Constrains water budget
Examples:
  Wells (pumping / injection)
  Recharge
  Interbasin flow
  No flow (discharge = 0)
    Groundwater divide
    Impermeable bedrock
    Impermeable fault zone
    Saltwater interface (coastal aquifer)

## Slide 13: Head-Dependent Flux Boundary
Flow rate into or out of aquifer varies in response to head changes
Specify head and boundary conductance
Represents leakage processes:
  General head (GHD) boundary
    Infinite source or sink
Q = C(Hb – H)
Q = Flux into or out of model (“aquifer”)
Hb = Boundary head (specified)
H = Head in GHB cell (simulated)
C = Conductance; C = K x (W x L) / D
H = Hb
Flux in/out of aquifer (Q)
Head in Aquifer (H)
Flux out of aquifer
H < Hb
Flux into aquifer
H > Hb
C = slope of line
0
+Q ►
◄ -Q

## Slide 14: Head-Dependent Flux Boundary
Represents leakage processes:
  Drain
    Infinite sink
Q = C(Hb – H)
Q = Flux out of model (“aquifer”)
Hb = Drain elevation (specified)
H = Head in drain cell (simulated)
C = Conductance; C = K x (W x L) / D
Hb
H
H
Qout = 0
H < Hb
Qout > 0
H > Hb
Hb
H = Hb
Flux in/out of aquifer (Q)
Head in Aquifer (H)
Flux out of aquifer
H < Hb
Flux into aquifer
H > Hb
C = slope of line
0
◄ -Q
+Q ►

## Slide 15: Head-Dependent Flux Boundary
Represents leakage processes:
  Evapotranspiration (EVT package)
    Finite sink
If H > HLS Q = Qmax
If Hex < H < HLS Q = C(Hex – H)
If H < Hex Q = 0
Q = Flux out of model (“aquifer”)
Qmax = Maximum ET flux (L/T) (specified)
HLS = Land-surface elevation (specified)
Hex = Extinction depth (specified)
H = Head in EVT cell (simulated)
C = Conductance; C = K x (W x L) / D
Q = Qmax
0 < Q < Qmax
Q = 0
Hex
HLS
H
H
H
Flux out of aquifer (Q)
Head in Aquifer (H)
Flux out of aquifer
C = slope of line
0
◄ -Q
Extinction depth
Land surface
Hex < H < HLS
H < Hex
H > HLS

## Slide 16: Head-Dependent Flux Boundary
Represents leakage processes:
  River / stream (RIV package)
    Finite source (losing)
    Infinite sink (gaining)
Hcell
Hbed
Hstage
Gaining: Hcell > Hstage
Hcell
Hbed
Hstage
Losing: Hbed < Hcell < Hstage
Hcell
Hbed
Hstage
Losing: Hcell < Hbed
Losing reach
Gaining reach
Head in Aquifer (H)
C = slope of line
Flux in/out of aquifer (Q)
0
+Q ►
◄ -Q
Hstage
Hbed
Flux out of aquifer (gaining river)
Flux into aquifer (losing river)
River

## Slide 17: Head-Dependent Flux Boundary
Stream Flow Routing (SFR) package features:
  Specified streamflow into the first stream reach
  Tributaries
  Points of diversion
  Gaining / losing reaches
  Precipitation, ET, and runoff on channel
  Groundwater & surface water accounting – stream can go dry
  Channel properties defined independently of grid
    Length of stream reach in model cell
    At upstream and downstream end of each reach:
      Streambed elevation, thickness, and K
      Channel width and depth
    Slope of channel
    Streambed and overbank roughness (Manning’s n)
    Unsaturated zone properties beneath streambed
      Initial and saturated volumetric water content
      Vertical saturated hydraulic conductivity
Niswonger and Prudic (2005)

## Slide 18: Head-Dependent Flux Boundary
Lake package (LAK) simulates lakes
Lake stage rises or declines from interaction with groundwater or streams simulated with SFR
Lake package accounts for:
  Precipitation, evaporation, and runoff from lake
  Pumping water to or from lake
  Lake properties can be defined independently of grid
    Separate text file can specify bathymetry
      Lake stage, surface area, volume
  Define initial, minimum, and maximum lake stages
  Lakebed leakance
Groundwater inflows and outflows from lake extracted from model output
Precipitation
Evaporation
Runoff
Groundwater IN
Water Table
Groundwater IN
Groundwater IN
Water Table
Climate
Net Pumping
Pumped Water IN/OUT
Terminal Pit Lake
(Hydraulic Sink)
A
Groundwater IN
Water Table
Groundwater OUT
Groundwater IN/OUT
Water Table
Flow-Through Pit Lake
B
Evaporation
Runoff
Climate
Net Pumping
Pumped Water IN/OUT
Precipitation

## Slide 19: Model Calibration
Matching simulated quantities to measured data by adjusting variables in model
Variables adjusted include:
  Hydraulic conductivity (K)
  Specific storage (Ss)
  Recharge / Discharge (W)
Better fit between simulated and measured data implies model results approximate reality

## Slide 20: Model Calibration: Types of Measured Data

## Slide 21: Measurement Observations
Water-level altitudes in evapotranspiration (ET) areas
  Measured WL assumed equal to land surface
  Specify ET rate in model
Discharge rate in playas
  Monitor discharge rate (actual rate uncertain)
  Specify WL as equal to land surface
Water-level altitudes in wells
Spring-pool altitudes
Land-surface altitudes
Devils Hole
(Halford and Jackson, 2020; fig. 46)
Notes: WL in ET area and perched springs: DEM that sampled 1:24,000 scale maps

## Slide 22: Measurement Observations
Vertical water-level differences
  Constrain vertical gradients
Lateral water-level differences
  Well-to-well
  Well-to-spring pool
  Constrain lateral gradients
(Halford and Jackson, 2020; fig. 49)

## Slide 23: Measurement Observations
Capture from ET areas
Capture from springs
Water-level declines in wells
(Halford and Jackson, 2020; fig. 57)

## Slide 24: Goodness of Fit
Good fit between measured and simulated data implies model adequately represents reality
Model calibration is a “data integration” exercise:
  Data consistency
  QA/QC of geology, pumpage, and water levels
  Misconceptions identified
(Halford and Jackson, 2020; fig. 54)
Notes: Simulated water levels compare favorably to measured water levels in DV3-SS model

## Slide 25: Goodness of Fit
Hydrograph Comparisons
  Should match magnitude and timing of water-level decline and recovery
  Matching shape of water-level trend demonstrates model adequately simulates aquifer stresses
(Halford and Jackson, 2020; figs. 66 & 67)

## Slide 26: QUIZ

## Slide 27: Question 1: Model Purpose
U = 0 µg/L
Problem:
  Anomalous uranium concentrations have been measured in 3 wells within study area
  Uranium source is unknown
Question posed:
  What is the source of uranium?
What is the most appropriate first step?
A) Build a model to determine uranium source
B) Analyze existing data to characterize groundwater, hydrogeology, and geochemistry
C) Multi-year field investigation to collect uranium data
Groundwater-flow direction
U = 0.009 µg/L
U = 0.028 µg/L
U = 0.012 µg/L
U = 0 µg/L
U = 0 µg/L
U = 0 µg/L

## Slide 28: Question 2: Model Development
True or False?
  It is not always necessary to develop a conceptual model prior to building a groundwater model.
  FALSE

## Slide 29: Question 3: Boundary Conditions
Pumping well
Monitoring well
Constant head boundary
Constant head boundary
Constant head boundary
Constant head boundary
Model purpose:
  Characterize the hydraulic properties of rock units, using drawdowns from a multiple-well aquifer test (Nevada)
Are the boundary conditions appropriate?
No
Why?
Constant head conceptualizes a rectangular island in the center of a lake
If drawdown propagates to constant heads, then an infinite supply of water can come into model domain
Hydraulic-property estimates degraded by incorrect conceptualization
10-foot drawdown contour

## Slide 30: Question 4: Boundary Conditions
For a steady-state model simulating predevelopment conditions…
Which boundary condition(s) are appropriate to simulate baseflow along a gaining reach of a perennial stream?
  A) River package (RIV)
  B) Drain package (DRN)
  C) Streamflow routing (SFR)
  D) General head (GHD)
  E) Constant head (CHD)
  F) Specified flow (WEL/RCH)
Water Table

## Slide 31: Question 5: Boundary Conditions
For a transient model simulating effects of pumping on streamflow…
Which boundary condition(s) are appropriate to simulate baseflow along a gaining reach of a perennial stream, which will go dry if 100% baseflow is captured?
  A) River package (RIV)
  B) Drain package (DRN)
  C) Streamflow routing (SFR)
  D) General head (GHD)
  E) Constant head (CHD)
  F) Specified flow (WEL/RCH)
Increase Pumping – Streamflow reduces to Zero

## Slide 32: Question 6: Boundary Conditions
Which boundary condition(s) are appropriate to simulate an ephemeral stream?
  A) River package (RIV)
  B) Drain package (DRN)
  C) Streamflow routing (SFR)
  D) General head (GHD)
  E) Constant head (CHD)
  F) Specified flow (WEL/RCH)

## Slide 33: Question 7: Calibration
Is the model fit to the data good or bad? Why?
  Bad – Simulated curve does not match the magnitude or shape of the water-level trend

## Slide 34: Question 8: Calibration
Is the model fit to the data good or bad? Why?
  Good – Simulated curve does match shape of water-level trend

## Slide 35: Question 9: Model Development
True or False?
  This model grid is appropriate for the hydrogeologic conceptualization
  TRUE
USGS fact sheet FS-127-97

## Slide 36: Summary
Groundwater models are developed to address questions
Conceptual model should be developed before groundwater model
Boundary conditions should consider model objective
Groundwater models are only as good as the data
Better fit between simulated and measured data implies model results approximate reality

## Slide 37: References
Domenico, P.A. and Schwartz, F.W., 1998, Physical and Chemical Hydrogeology. 2nd Edition, John Wiley & Sons Inc., New York, 506 p.
Freeze, R.A. and Cherry, J.A., 1979, Groundwater. Prentice-Hall Inc., Englewood Cliffs, Vol. 7632, 604 p.
Garcia, C.A., Jackson, T.R., Halford, K.J., Sweetkind, D.S., Damar, N.A., Fenelon, J.M., and Reiner, S.R., 2017, Hydraulic characterization of volcanic rocks in Pahute Mesa using an Integrated Analysis of 16 multiple-well aquifer tests, Nevada National Security Site, 2009–14: U.S. Geological Survey Scientific Investigations Report 2016-5151, 62 p., https://doi.org/10.3133/sir20165151
Halford, K.J., and Jackson, T.R., 2020, Groundwater characterization and effects of pumping in the Death Valley regional groundwater flow system, Nevada and California, with special reference to Devils Hole: U.S. Geological Survey Professional Paper 1863, 178 p., https://doi.org/10.3133/pp1863
Halford, K.J., Stamos, C.L., Nishikawa, T. and Martin, P., 2010, Arsenic Management Through Well Modification and Simulation. Groundwater, 48: 526-537. https://doi.org/10.1111/j.1745-6584.2009.00670.x
Halford, K., van Niekerk, J., and van Coller, A., 2025, Potential Effects Of Leeville Expansion And Concurrent Dewatering In The Carlin Trend, Nevada: Digby Wells technical memorandum, prepared for Nevada Gold Mines LLC, 64 p.
Harbaugh, A.W., 2005, MODFLOW-2005, the U.S. Geological Survey modular ground-water model—The ground-water flow process: U.S. Geological Survey Techniques and Methods, book 6, chap. A16, https://doi.org/10.3133/tm6A16
Heath, R.C., 1983, Basic ground-water hydrology: U.S. Geological Survey Water Supply Paper 2220, 84 p. https://doi.org/10.3133/wsp2220
Jackson, T.R., Fenelon, J.M., and Paylor, R.L., 2021, Groundwater flow conceptualization of the Pahute Mesa–Oasis Valley Groundwater Basin, Nevada—A synthesis of geologic, hydrologic, hydraulic-property, and tritium data: U.S. Geological Survey Scientific Investigations Report 2020–5134, 100 p., https://doi.org/10.3133/sir20205134
Jackson, T. R., Halford, K. J., Gardner, P. M., and Garcia, C.A., 2018, Evaluating micrometeorological estimates of groundwater discharge from Great Basin desert playas: Groundwater, v. 56, no. 6, p. 909–920, https://doi.org/10.1111/gwat.12647
Johnson, A.I., 1967, Specific Yield – Compilation of Specific Yields for Various Materials: U.S. Geological Survey Water-Supply Paper 1662-D, 80 p.
Joseph, T., Godwin, T., McManus, D., Nordberg, M., Shannon, H., and Stringhorn, S., 2016, Best Management Practices for the Sustainable Management of Groundwater, Hydrogeologic Conceptual Model: State of California, California Natural Resources Agency report, 25 p.
Niswonger, R.G. and Prudic, D.E., 2005, Documentation of the Streamflow-Routing (SFR2) Package to include unsaturated flow beneath streams--A modification to SFR1: U.S. Geological Survey Techniques and Methods, Book 6, Chap. A13, 47 p.
Rivera, A., 2014, Chapter 2 of Groundwater Basics in Canada’s Groundwater Resources, ed., A. Rivera: Fitzhenny and Whiteside, Markham, Ontario, Canada, p. 24 -61.

## Slide 38: Review of Hydraulic Property Fundamentals

## Slide 39: Transmissivity
Transmissivity (T): capacity of an aquifer to transmit groundwater
T = Hydraulic conductivity (K) x aquifer thickness (b)
Darcy’s Law:
T
Water table
h2
h1
L
Q = Groundwater-flow rate
K = Hydraulic conductivity
A = Cross-sectional area of aquifer
Δh = Head difference between wells
L = Distance between wells
w = Width of aquifer
(Heath, 1983)

## Slide 40: Transmissivity
T
T
High transmissivity: farther apart water-level contours
High transmissivity: increased groundwater flow
(Jackson, et al, 2021)

## Slide 41: Storativity
Storativity (S): volume of water an aquifer releases from or takes into storage per unit surface area of the aquifer per unit change in head
Related to porosity
Porosity
Specific Yield
Sy = Specific yield
Water stored in pore space that will drain by gravity
Sr = Specific retention
Water stored in pore space that remains as film on rock surface
**Sy sometimes used as “effective porosity” in contaminant transport
(Heath, 1983)

## Slide 42: Storativity: Unconfined Aquifer
Soil Zone
Unsaturated Zone
Water Table
Saturated Zone
Unconfined aquifer
Storativity ~ Specific Yield
Unconfined aquifers do not have a confining unit between land surface and saturated zone
Top of aquifer is water table
Sy
Sr
(Heath, 1983)

## Slide 43: Storativity: Confined Aquifer
Storativity = Specific Storage x Aquifer thickness
Confined aquifer:
  Overlain and underlain by low-K confining units
  Confining units cause aquifer to be under pressure
  When aquifer penetrated by well, increased pressure causes water level to rise above top of aquifer to a potentiometric surface
Soil Zone
Unsaturated Zone
Water Table
Unconfined aquifer
Confining unit
Confined aquifer
Potentiometric surface
Aquifer thickness
(Heath, 1983)

## Slide 44: Storativity: Confined Aquifer
Confined Aquifer
Confining Unit
Storativity = Specific Storage x Aquifer thickness
  Confining units cause aquifer to be under pressure
Pumping causes depressurization of aquifer
Specific Storage = water released from storage due to:
  Expansion of water
    Remove water by pumping (depressurization)
    Remaining water ( Pressure Volume)
Confining Unit
Total load on aquifer (σtotal)
Support through water (p)
σtotal = σs + p
Support through rock skeleton (σs)
Constant
(Heath, 1983)

## Slide 45: Storativity: Confined Aquifer
Confined Aquifer
Confining Unit
Storativity = Specific Storage x Aquifer thickness
  Confining units cause aquifer to be under pressure
Pumping causes depressurization of aquifer
Specific Storage = water released from storage due to:
  Expansion of water
    Remove water by pumping (depressurization)
    Remaining water ( Pressure Volume)
  Compression of aquifer skeleton
    Increase stress on aquifer skeleton
    Reduces pore space
Confining Unit
Total load on aquifer (σtotal)
Support through water (p)
σtotal = σs + p
Support through rock skeleton (σs)
Constant
(Heath, 1983)

## Slide 46: Storage difference: Unconfined Vs. Confined
Sy = fraction of saturated void space that drains
Drained water is from narrow cone of depression
Ss = aquifer compressibility - that is, water released by depressurizing the aquifer per unit head
Although Ss << Sy, volumes pumped from aquifer can be very high because pressure release can propagate far into aquifer, in all directions
Water table
Cone of depression
Confining bed
Unconfined aquifer
Cone of depression
Confining bed
Confined aquifer
Confining bed
Potentiometric surface
Land surface
Lateral extent of cone
Unconfined: S = Sy + Ssb
S ~ Sy = 0.01 to 0.4
Confined: S = Sy + Ssb
S = Ssb = 10-6 to 10-3
small
N/A

## Slide 47: Storativity – Typical Estimates
Data from Johnson (1967), Rivera (2014), Freeze and Cherry (1979), and Domenico and Schwartz (1998)
Storativity values have a narrow range of estimates for each rock type

## Slide 48: Question 10: Hydraulic Properties
True or False?
  Because Ss << Sy, the amount of water that can be pumped from a confined aquifer will always be less than an unconfined aquifer.
  FALSE