## Slide 1: Obtaining Useful Answers from Groundwater Models:    Flow Models & Calibration
Keith J Halford, Carson City, NV
Tracie Jackson, Henderson, NV

## Slide 2: FLOW MODELS ─●─ Consistent Stories—Not Data

## Slide 3: Numerical Methods
General, less exact numerical solution traded for exact and limited analytical solution
Minor limitation given that both solutions are inexact approximations of reality
Carve model domain into many small boxes
Flow between boxes defined by Darcy’s Law
Darcy’s Law
Area of Interest /
Model Domain

## Slide 4: Groundwater Models
Models balance mass
1-block crudest case, i.e. a water-budget
Want to know more
  Divide into small blocks / cells
  Equations connect, ), Darcy’s law
Evapotranspiration
Pumpage
Precipitation

## Slide 5: Price of Details
Added detail requires additional knowledge
Where and when
  Recharge / evapotranspiration (ET)
Rivers & springs
  Flows & stages
Where are wells
  Quantity & timing of pumping
Distribute hydraulic properties
  Transmissivity / hydraulic conductivity
  Specific yield & specific storage

## Slide 6: Define an Area
Encompass problem
  New pumping & spring of concern
  Contamination & potential receptors
Expand to nearest well-defined, boundaries
  No-flow by low permeability or groundwater divide
  Specified head—Major river, lake, ocean, Minimal utility in Nevada
Consider liabilities if simulating the world
  More features to define/make-up
    Hydraulic properties, recharge, springs, etc.
  More likely to reveal ignorance

## Slide 7: Surface-Water Problem
Problem
  Freshwater releases affect oyster beds
Develop 2-D model of Sebastian River
  Model simulates areal mixing
  Measurements show vertical stratification much more significant than areal mixing
  Much consternation
Concerns about approach, Not relevant
Oyster beds — Outside of model
  Scrapped model
  Replaced with statistical analysis
1 MILE
Sebastian River
Oyster Beds
(Wicklein and Gain, 1999)

## Slide 8: Must Be Inside Model
Nuclear testing in Yucca Flat, Nevada
  Radionuclide transport in groundwater
  Define contamination extent during 1,000 yrs
  Tritium defines extent, limited to ~150 yrs
Develop calibrated flow model
  Transport from a dozen detonations
  Simulated plume hits model edge, Extent undefined
Not uncommon mode of failure
Features & results must be inside model
Seems stupid; IT IS — Ask questions
BOOM!
150 MILES
5 MILES
N
Transport time, in years
0
1,000
150
500
?
(Navarro-Intera, LLC, 2013; fig. 5-49)

## Slide 9: Lateral Extent—Just So
Enough for problem, without simulating the world
Extents of regional models for radionuclide transport from NNSS must encompass,
  Nuclear tests & plausible receptors (springs)
4 model extents ranged from 7,800 to 15,900 mi²
  2D-FE (Waddell, 1982)
    Adequate, but doubts remained about flow from north of NNSS
  UGTA (IT Corporation, 1997)
    Boundary extended north, more water-levels
  DVRFS.v1 (Belcher, 2004), Expansion not needed, BUT
    Pahrump fairly added for what-abouts…
    Modeling by committee added remainder, Little supporting data
    Unknown expansion by specified heads on all edges
  DV3, (Halford and Jackson, 2020)
    Pared back to primary objectives,
    Transport of radionuclides &
    Effects of pumping on water levels in Devils Hole
50 MILES
2D-FE
UGTA
DVRFS.v1
DV3
Devils
Hole

## Slide 10: Discretization
Aquifer extent defined by physical features
  Geologic contact
  Groundwater divide
Arbitrary grid overlain— Details unimportant
  OK, provided a few cells occur between stress & problem
  Cells can be shapes other than squares
Remove cells beyond aquifer
Grid generation needs to be easy
AQUIFER EXTENT

## Slide 11: Distributions, Not Points
Regardless of ignorance
  Geology defined throughout a model
  Hydraulic properties defined everywhere
    Primarily transmissivity & storage coefficient
  Recharge, evapotranspiration (ET), pumpage, streams
    All must be defined—All places, All times
Real geologic information invaluable
  Basis of story telling
  Eliminate the craziest stories

## Slide 12: Geohydrologic Framework
Extrapolating hydraulic properties
  Limited hydrologic information
  Basis of stories that dominate without data
Geology simple, 2000 ft
  Must assign thickness in model
  Estimating T, not K, of hard rocks
Extent & thickness of upper basin fill, Useful extrapolator,
Thin upper layer for hydraulics, Not varying K & S
(Halford and Plume, 2011)

## Slide 13: Divide & Distribute
Eagle Valley, Nevada
Simulate basin fill, Hardrock impervious
Divide into squares
Mountain front recharge, add water
  Simulate big channels
  Generalize runoff from small drainages
Discharge, remove
  ET areas & Carson River
Wells
  Pumping—Known stress
  Observation—Calibration
1 MI

## Slide 14: Software
Must assure that 2 + 2 = 4
Vanilla code desirable
  Documented & downloadable
  Cite reference to report
  Support exists
MODFLOW—Groundwater flow
  Started +40 yrs ago; OFR83-875
  MODFLOW-2005; standard ~15 yrs
  MT3D added transport; 1990
  MODFLOW6; flow & transport
Known code; One less argument

## Slide 15: CALIBRATION

## Slide 16: Aquifer Test Example
Single-well analysis, Cooper-Jacob (1946)
  Model is a straight line
  Adjust offset (S) & slope (T)
Calibration
  Minimize differences between measurements & straight line
  Eyeball difference, ignore what model cannot explain
Faith in T depends on fit
T = 1,500 ft²/d

## Slide 17: Parameter Estimation
Formal methods for calibration discussed as parameter estimation
  T & S were parameters in previous example
Eyeballing
  Possible with 2 parameters, more sensible even
  Suicidal with 100s or 1,000s of parameters
Same concepts for formal procedures
  Minimizing differences between model & reality
  Replace “eyeballing” with equation
  Judgment still embedded in equation

## Slide 18: Objective Function
Machine is stupid; Needs numbers
Quantifies differences between simulated & measured values
Basis for estimating parameters
  Recharge
  Transmissivity
  Storage coefficient
Sum-of-squares, A measure of misfit
“Objective” is a goal, NOT unbiased
Weights control observation importance
  Considers data type & quality
  Defined iteratively during calibration
  Reflect your preferred emphasis
SIMULATED
Head, Flow, T
Number of
Observations
MEASURED
Head, Flow, T
Weight
(Your Judgment)
Makes
Hi or Low
Bad

## Slide 19: Weights
How many unique observations?
  Designing pump-and-treat at site A — 11
  Regional study — 2 to 3
Balance differences between units
Just numbers to machine
  Heads ignored without “equalizing” flows
It hurts, but one must think & explain
AQUIFER
EXTENT
OBSERVATION
WELL
B
A

## Slide 20: Arrays
Distribute hydraulic properties
  Must fill entire model
  Specify in arrays, many values
  Can change cells from squares to other shapes, same extrapolation problem
Eagle Valley example
  186 by 130 = 24,180 cells
  Active cells still 12,183 values
  Less than 200 wells
Numbers exceed ignorance, Must extrapolate
1 MI

## Slide 21: Parameters to Arrays
Define hydraulic properties (T,S,...)
  Relatively few values specified & estimated
  Extrapolate from parameters to arrays
Two primary methods
  Zones, Single value in area
  Pilot points, Smoothly vary from points
Demonstrate with simple array
  Arrays indexed from upper, left
  Values at cell—head (h), T, S
  Calculate between nodes—Q
  Safer if rows ≠ columns, Bad demo

## Slide 22: Zones
Similar features grouped— Basin fill, bedrock
Map features with integers
Pair hydraulic conductivity (K) with integers
Create array of K
  Locate zone number
  Find K in zone-K table
  Assign K at (row, column)
Parameters are K in zone-K table
Resulting array
  Homogeneous in a zone
  No interpolation between zones

## Slide 23: Pilot Points (PP)
Interpolate in a unit—Basin fill or bedrock
Specify hydraulic conductivity (K) on map
  Row, column simplification
  Usually coordinates, UTM
  Independent of grid
Create array of K
  Distances from PP to K-parameter
  Calculate weights, inverse distance
  K = weight * K-parameter at each PP
Parameters are K in PP table
Resulting array
  Smoothly variable in a zone

## Slide 24: Pilot Points & Zones
Merit in both approaches
Zones — Sharp K contrast
  Bedrock / basin-fill contact
  No interpolation between materials
Pilot points — Gradational or Unknown K change
  Coarse-grain to fine-grain
  Subsurface change fuzzy
  Contrast not extreme
  Constrain K estimates with stories, KSAND ~ 100*KPLAYA
Sharp Contact
Gradational Contact
20 MILES
(Halford and Plume, 2011)

## Slide 25: Quantifying Calibration
DOES
Dump work on computer
Test more alternatives
  Invalidate more bad ideas
  Twiddle knobs less
Rub nose in data limitations
Enforces consistency & repeatability
DOES NOT
Automatically improve estimates
Eliminate subjectivity

## Slide 26: Tube Model
Calibration example
Reality, physical model
  Solve numerical model
    Workbook, 02_Tube_Model-WL_Profiles.xlsm
Topics
  Defining parameters
  Evaluating misfit
  Weighting observations

## Slide 27: References
Belcher, W.R., ed., 2004, Death Valley regional ground-water flow system, Nevada and California—Hydrogeologic framework and transient ground-water flow model: U.S. Geological Survey Scientific Investigations Report 2004-5205, 408 p., https://pubs.er.usgs.gov/publication/sir20045205
Cooper, H.H. and C.E. Jacob, 1946. A generalized graphical method for evaluating formation constants and summarizing well field history, Am. Geophys. Union Trans., vol. 27, pp. 526-534.
Halford, K.J., and Plume, R.W., 2011, Potential effects of groundwater pumping on water levels, phreatophytes, and spring discharges in Spring and Snake Valleys, White Pine County, Nevada, and adjacent areas in Nevada and Utah: U.S. Geological Survey Scientific Investigations Report 2011-5032, 52 p. https://doi.org/10.3133/sir20115032
Halford, K.J., and Jackson, T.R., 2020, Groundwater characterization and effects of pumping in the Death Valley regional groundwater flow system, Nevada and California, with special reference to Devils Hole: U.S. Geological Survey Professional Paper 1863, 178 p., https://doi.org/10.3133/pp1863
Harbaugh, A.W., 2005, MODFLOW-2005, the U.S. Geological Survey modular ground-water model—the Ground-Water Flow Process: U.S. Geological Survey Techniques and Methods, book 6, chap. A16, variously paged, accessed June 27, 2017, at https://pubs.usgs.gov/tm/2005/tm6A16/
Harbaugh, A.W., and McDonald, M.G., 1996, User’s documentation for MODFLOW-96, an update to the U.S. Geological Survey modular finite-difference ground-water flow model: U.S. Geological Survey Techniques of Water-Resources Investigations, book 6, chap. A1, 586 p. https://doi.org/10.3133/ofr96485
Harbaugh, A.W., Banta, E.R., Hill, M.C., and McDonald, M.G., 2000, User guide to modularization concepts and the Ground-Water Flow Process, MODFLOW-2000 the U.S. Geological Survey modular ground-water model: U.S. Geological Survey Open-File Report 00–92, 121 p., https://pubs.er.usgs.gov/publication/ofr200092
IT Corporation, 1997, Regional groundwater flow and tritium transport modeling and risk assessment of the underground test area, Nevada Test Site, Nevada: Report DOE/NV-477 prepared by the IT Corporation, Las Vegas, Nevada, for the U.S. Department of Energy Nevada Operations Office [variously paged], https://www.osti.gov/biblio/788792
Langevin, C.D., Hughes, J.D., Banta, E.R., Niswonger, R.G., Panday, Sorab, and Provost, A.M., 2017, Documentation for the MODFLOW 6 Groundwater Flow Model: U.S. Geological Survey Techniques and Methods, book 6, chap. A55, 197 p., https://doi.org/10.3133/tm6A55
McDonald, M.G. and A.W. Harbaugh, 1984, A modular three-dimensional finite-difference ground-water flow model: U.S. Geological Survey Open-File Report 83-875, 528 p. https://doi.org/10.3133/ofr83875
Navarro-Intera, LLC, 2013, Phase I flow and transport model document for Corrective Action Unit 97—Yucca Flat/Climax Mine, Nevada National Security Site, Nye County, Nevada, Rev. 1: Las Vegas, Nevada, Navarro-Intera Report N-I/28091-080, https://www.osti.gov/scitech/biblio/1094979
Southern Nevada Water Authority, 2009, Transient numerical model of groundwater flow for the Central Carbonate Rock Province—Clark, Lincoln, and White Pine Counties Groundwater Development Project. Prepared in cooperation with the Bureau of Land Management: Southern Nevada Water Authority, Las Vegas, Nevada, 394 p.
McDonald, M.G., and Harbaugh, A.W., 1988, A modular three-dimensional finite-difference ground-water flow model: U.S. Geological Survey Techniques of Water-Resources Investigations, book 6, chap. A1, 586 p., https://pubs.er.usgs.gov/publication/twri06A1
Waddell, R.K., 1982, Two-dimensional, steady-state model of ground-water flow, Nevada Test Site and vicinity, Nevada-California: U.S. Geological Survey Water-Resources Investigations Report 82-4085, 72 p., 1 pl., https://doi.org/10.3133/wri824085
Wicklein, S.M., and Gain, W.S., 1999, Probability analysis of the relation of salinity to freshwater Discharge in the St. Sebastian River, Florida: U.S. Geological Survey Water-Resources Investigations Report 99-4003, 37 p. https://doi.org/10.3133/wri994003
Zheng, Chunmiao, and Wang, P.P., 1999, MT3DMS—A modular three-dimensional multi-species transport model for simulation of advection, dispersion and chemical reactions of contaminants in groundwater systems; Documentation and user’s guide: Contract report SERDP–99–1: Vicksburg, Miss., U.S. Army Engineer Research and Development Center, 169 p. https://hydro.geo.ua.edu/mt3d/index.htm