## Slide 1: Obtaining Useful Answers from Groundwater Models: Hydraulic Properties & Geologic Frameworks
Tracie R Jackson, Henderson, NV
Keith J Halford, Carson City, NV

## Slide 2: Geologic Frameworks Vs Groundwater Models
Purpose of geologic frameworks:
  Distribute hydraulic properties (K, Sy, Ss)
  Groundwater-flow model
Geologic Framework

## Slide 3: Approaches to Distribute Hydraulic Properties
Homogeneous K in each geologic unit (zone)
Heterogeneous K in each geologic unit (zone)
Pilot point
K, ft/d

## Slide 4: Geologic Framework Misconceptions
Mapped faults and fractures define flow
Geology can always be used as a surrogate for hydraulic conductivity
Adding geologic details improves hydrologic understanding

## Slide 5: Mapped Faults & Fractures Define Flow
Misconception #1

## Slide 6: Floridan Aquifer Example
10 ft
Imaged
Fracture
Visual observation of fractures/voids not correlated with K
K controlled by hydraulic connections
Flow log needed to inform K
K not proportional to obvious features
  Imaged fractures, K ~ 2,000 ft/d
  Caverns in Ocala, K ~ 200 ft/d
OR621
OR640
1,000
SEA
LEVEL
FEET
0
5,000
0
FLOW RATE, IN GPM
Ocala Limestone
Avon Park
10 ft
(Spechler and Halford, 2001)

## Slide 7: Geology is Always a Surrogate for Hydraulic Conductivity
Misconception #2

## Slide 8: Hydraulic Conductivity (K)
K range poorly predicted for hard rocks
Igneous, metamorphic, and carbonate rocks can be aquifers or confining units
K range better predicted for unconsolidated rocks (gravel, sand, clay)
( Suwai, 2016)
Aquifer
Confining Unit

## Slide 9: Detailed, Complex Geologic Frameworks Improve Hydraulic-Conductivity Estimates
Misconception #3

## Slide 10: Complex Geologic Framework
Pahute Mesa–volcanic terrain
Hydraulic data inform 37 of 77 units
( Garcia et al, 2017)

## Slide 11: Hydraulic-Conductivity (K) Distributions
Highly heterogeneous hydrostratigraphic units:
  Units are hydraulically similar
  Geometric mean K estimates are within an order of magnitude
  Complex geologic framework does not improve differentiation between aquifers and confining units
( Garcia et al, 2017)

## Slide 12
Transmissivity and Groundwater Models

## Slide 13: Groundwater Flow
MODFLOW solves groundwater-flow equations
Vertically integrated hydraulic properties:
  Transmissivity,
  Storativity, S — Compressibility & Drainage
T & S estimated from aquifer tests
No geology term, Limited by correlation to T & S
(Harbaugh, 2005)

## Slide 14: Transmissivity versus Hydraulic Conductivity
Transmissivity (T) = Hydraulic conductivity (K) x aquifer thickness (b)
T estimated quantity, not K
Aquifer thickness (b) unknown and K estimates will differ if use
  Depth Drilled
  Screen Length
  Aquifer Thickness in Hydrogeologic Model
T
K
Example
T = 1,000 ft²/d
If b = well screen = 10 ft
K = 1,000 ft²/d/10 ft = 100 ft/d
If b = aquifer thickness = 1,000 ft
K = 1,000 ft²/d/1,000 ft = 1 ft/d
Transmissivity, Estimate unchanged!

## Slide 15: Transmissivity (T) and Rock Type
Rock types have unique hydraulic variability
Carbonate rocks
Volcanic rocks
Basin fill
Low-permeability rocks
Transmissivity, in feet squared per day
(Halford and Jackson, 2020; fig. 21)

## Slide 16: Transmissivity (T) and Rock Type
Median T of carbonates, volcanics, and basin fill are ~1,000 ft²/d, but variability differs markedly
Rock type reliably establishes maximum likely T
Carbonate rocks
Volcanic rocks
Basin fill
Low-permeability rocks
Transmissivity, in feet squared per day
(Halford and Jackson, 2020; fig. 21)

## Slide 17: Compare Transmissivity
(Fenelon et.al., 2016; figs. 6 & 12)

## Slide 18: Summary
Geologic frameworks used to distribute hydraulic properties
Groundwater flow controlled by hydraulically connected fractures, not by number / size of fractures
Detailed, complex frameworks do not improve hydraulic-property estimates
Compare transmissivity, not hydraulic conductivity, to rock types
  Informs range of expected transmissivity estimates in groundwater model

## Slide 19: References
Fenelon, J.M., Halford, K.J., and Moreo, M.T., 2016, Delineation of the Pahute Mesa–Oasis Valley groundwater basin, Nevada (ver. 1.1, May 2016): U.S. Geological Survey Scientific Investigations Report 2015–5175, 40 p., http://dx.doi.org/10.3133/sir20155175
Garcia, C.A., Jackson, T.R., Halford, K.J., Sweetkind, D.S., Damar, N.A., Fenelon, J.M., and Reiner, S.R., 2017, Hydraulic characterization of volcanic rocks in Pahute Mesa using an Integrated Analysis of 16 multiple-well aquifer tests, Nevada National Security Site, 2009–14: U.S. Geological Survey Scientific Investigations Report 2016-5151, 62 p., https://doi.org/10.3133/sir20165151
Halford, K.J., and Jackson, T.R., 2020, Groundwater characterization and effects of pumping in the Death Valley regional groundwater flow system, Nevada and California, with special reference to Devils Hole: U.S. Geological Survey Professional Paper 1863, 178 p., https://doi.org/10.3133/pp1863
Harbaugh, A.W., 2005, MODFLOW-2005, the U.S. Geological Survey modular ground-water model—The ground-water flow process: U.S. Geological Survey Techniques and Methods, book 6, chap. A16, https://doi.org/10.3133/tm6A16
Jackson, T.R., Fenelon, J.M., and Paylor, R.L., 2021, Groundwater flow conceptualization of the Pahute Mesa–Oasis Valley Groundwater Basin, Nevada—A synthesis of geologic, hydrologic, hydraulic-property, and tritium data: U.S. Geological Survey Scientific Investigations Report 2020–5134, 100 p., https://doi.org/10.3133/sir20205134
Spechler, Rick M., and Halford, Keith J., 2001, Hydrogeology, Water Quality, and Simulated Effects of Ground-Water Withdrawals from the Floridan Aquifer System, Seminole County and Vicinity, Florida: Water-Resources Investigations Report 01-4182, 116 p. https://doi.org/10.3133/wri014182
Suwai, J., 2016, Basic hydrogeology in geothermal systems: SDG Short Course I on Exploration and Development of Geothermal Resources, organized by UNU-GTP, GDC and KenGen, at Lake Bogoria and Lake Naivasha, Kenya, Nov. 10-31, 2016