## Slide 1: Obtaining Useful Answers from Groundwater Models:    Looking & Comparing Required
Keith J Halford, Carson City, NV
Tracie Jackson, Henderson, NV

## Slide 2: Goodness of Fit
Calibration should be evaluated with more than basic statistics
  Observation type, count, min, max,…
  Root-mean-square (RMS) common measure of fit
Basic charts provide context
  RMS error compared to range
  Still limited to formal observations
Model plausibility also rests on unquantified results
  Add complete time series to hydrographs
(Halford and Jackson, 2020)

## Slide 3: Hydrographs—Extend
Measured and simulated water levels in objective function usually plotted
  Typically from PEST files
Time series exist during entire simulation period
Extract extended hydrograph
  Extend PEST observations with “dummy” measurements & weight to 0, Negates influence on calibration
  Extract from node in MODFLOW6 with Observation (OBS) Utility
(Davis, et al., 2025)

## Slide 4: Hydrographs—Shift
Principally compare trends between measured & simulated changes
Big errors can thwart comparison
Shift simulated water levels
  Average differences used
  Alternatively, shift at 1 measurement
Report shift in hydrograph
  Avoids confusing author & reader
Extending time series clarifies simulated recharge signal
Measured averages 6,881 ft
Simulated averages 5,539 ft
Add 1,342 ft
(Davis, et al., 2025)

## Slide 5: Hydrographs—Gaps
Measured water-levels have gaps
  Estimate with dashed lines if clueless
Simulated water levels should be informed by stresses, usually,
  Pumping
  Recharge
Simulated response could depart from simple interpolation
Extended time series needed to see all simulated changes
  Interpolation of simulated response is not acceptable
(Davis, et al., 2025)

## Slide 6: Checking ─●─ Quantified & Fuzzy

## Slide 7: Hydraulic Property Estimates
Tabulated summaries of hydraulic properties work for simple models
  Theis for example,
    T = 1,000 ft²/d &
    S = 0.001
  Suffices for homogeneous & isotropic
Spatially distributed estimates not amenable to tables
  Letter of law met, not comprehensible
  Spatial identifiers in table solid indicator that table wasn’t a good idea

## Slide 8: Maps More Useful
3D view not needed after layering defined
  Vertical sequence knowable for a few units
Map more informative than colored shapes floating in a white void
Display lateral extents of units, all depths
K & S manipulated between estimated values and model
Need to see input as used by model
5 MILES
(Halford and Jackson, 2020)

## Slide 9: Display Transmissivity
Transmissivity, T, integrates K & b
  Directly comparable to aquifer-test results
  Maps better than K
Total T summarizes state
Details displayed by mapping T of each unit
Add pilot points & show estimated parameters
Differentiate K & b, in details
Total Transmissivity
Shallow Basin Fill
Deep Basin Fill
Volcanic Sedimentary Rocks
Shallow Carbonate Rocks
5 MILES
(Halford and Jackson, 2020)

## Slide 10: Compare Transmissivity
Formally compare transmissivity, Add to objective function
  Location specific
  Analogous to streamflow
Under simulating range consistent with broad limits on estimated K, rather than honoring T observations
Transmissivity observations
  Improve low-T areas, As important as high-T areas
  Increase simulated range
20 MILES
(Halford and Jackson, 2020)

## Slide 11: Hydrographs
Typically check hydrographs, See if they, “Look funny” – In addition to quantified errors
ER-6-1 #2 aquifer test as an example
Tracer 3 is 33 miles from ER-6-1 #2, Fit declared good or bad on shape as well as RMS
15 MILES
ER-6-1 #2

## Slide 12: Water-Level Profiles
Anomalous water levels around well AD-4a
  Mapped +60 years ago
  Data sparse east of well AD-4a
  Coarse basin fill abuts carbonate rocks
Carbonate water upwells & flows into basin fill
Well AD-4a corridor
  Q = 2,000 acre-ft/yr (Fenelon et al, 2016)
  Passes ~80% of interbasin flow
Corridor defined by water levels & specific capacity in basin fill
Pumping west of well AD-4a affects water levels in Devils Hole
Significant hydraulic feature, Needs to be simulated correctly
(Classen 1985, Modified from Walker & Eakin, 1963)
2300
2350
2200
2350
2100
West
East
South
North
P
5 MILES

## Slide 13: Conventional Comparison
Water levels include
  Measurements in wells & spring pools
RMS error in wells
  DV2 = 230 ft
  DV3 = 48 ft
  Looks bad, but effect is?
Interbasin flow through well AD-4a corridor
  DV2 underestimates water levels
  Simulated contours & T differ
  Residuals appear similar
DV2
DV3
Well AD-4a
Corridor
5 MILES

## Slide 14: Compare Profiles
DV2 poorly simulates profiles
  RMS error ~35 ft small relative to overall RMS error
  AD-4a corridor not apparent in simulated profiles
DV3 results resemble measured
  Local water-level errors differ greatly from overall model error
  Simulated & measured water-level profiles agree
  Simulated flow in AD-4a corridor similar to field estimates
2350
2300
2200
5 MILES
DV2
2350
2300
2200
5 MILES
DV3
2350
West
East
South
North

## Slide 15: Unmeasured Badness
Model top frequently is water table
  Initially a contoured surface
  Conceptual model of recharge & permeability
  Numerical surface differs, forced consistency
Check difference
  Replace conceptual array with simulated water table
  Differences exist, but still OK
Really bad possible
  Minor flow effect, Low-K
  Major acceptance problem
Conceptual
OK Numerical
BAD Numerical
Notes: 585 x 480 pixels

## Slide 16: Present Results ─●─ Pictures are quicker

## Slide 17: Drawdown Extent
Cumulative water-level declines from pre-development to 2018 in response to historical pumping
Drawdowns contoured to 1 ft
  Unusually small drawdown
  Small threshold because of Devils Hole
Drawdown limit 5-10 ft more consistent with natural fluctuations
40 MILES
N
(Halford and Jackson, 2020)

## Slide 18: Predevelopment water budgets
Estimate subarea water budgets
Water budgets inform groundwater velocities and water availability in subareas
Subareas mapped using pathlines, water-level contours, and existing mapped basin boundaries
Map clarifies direction & location of flows across boundaries
40 MILES
N
(Halford and Jackson, 2020)

## Slide 19: Yucca Flat
10 MILES
N
(Halford and Jackson, 2020)

## Slide 20: Pathlines—Manager Simple
Flow to Furnace Creek area important to National Parks
  Flow simulated by DV2 & DV3 models
  Geochemistry of Furnace Creek springs
    60% from AFFCR basin
    40% from Ash Meadows basin
  Identify most plausible model
Backtrack paths from Furnace Creek
  Flow-weighted pathlines
  Color by originating basin
  Results need little explanation
DV3 pathlines remain plausible
Pahrump
Valley
Pahute Mesa-
Oasis Valley
40 MILES
Ash
Meadows
AFFCR
Furnace Creek Area
DV2
DV3
N
(Halford and Jackson, 2020)

## Slide 21: Attributing Effects
Attribute drawdown in Devils Hole to grouped pumping wells
Group wells into pumping centers
  11 pumping centers created
  1 simulation per pumping center
    Just pumping center wells simulated
    Drawdown in Devils Hole recorded
  6 pumping centers affect Devils Hole
Annual pumping from AFFCR & Ash Meadows basins
  Increased from <1,000 to 19,000 acre-ft between 1950 and 2000
  Relatively steady after 2000
Pahrump
Valley
Pahute Mesa-
Oasis Valley
40 MILES
Ash
Meadows
AFFCR
(Halford and Jackson, 2020)
N
Megachannel
Devils
Hole
Outside
Megachannel
Indian
Springs
Central
Amargosa
Desert
Cappaert
Enterprises
Inside
Megachannel
Crystal

## Slide 22: Volume & Location
Drawdown not proportional to volume pumped and proximity to Devils Hole
Megachannel major factor
  Big drawdown from Crystal & NNSS wells inside megachannel
  Distance mutes Amargosa Desert
  Cappaert Enterprises biggest
Attribution shows effect of other pumpers on total
  Individual drawdowns do NOT sum to composite result
Same concept for stream capture
Cappaert Enterprises
(Modified from Halford and Jackson, 2020)
Central Amargosa Desert
Central Amargosa Desert
Inside Megachannel
Crystal

## Slide 23: Conclusions
Looking necessary
  Evaluate calibration with more than statistics
  Better models—Find difficult to define badness
  Easier comprehension from users —Calibration & results
More looking with cheap tools
  Google Earth—Fast & does not spook managers
  Comprehend charts & maps faster than tables
Add to standard pictures
  Transmissivity aids comprehension & mappable
  Water-level profiles — Hydrographs for steady state
Cross the bar of “Not obviously wrong”

## Slide 24: References
Belcher, W.R., ed., 2004, Death Valley regional ground-water flow system, Nevada and California—Hydrogeologic framework and transient ground-water flow model: U.S. Geological Survey Scientific Investigations Report 2004-5205, 408 p., https://pubs.er.usgs.gov/publication/sir20045205
Belcher, W.R., Sweetkind, D.S., Faunt, C.C., Pavelko, M.T., and Hill, M.C., 2017, An update of the Death Valley regional groundwater flow system transient model, Nevada and California: U.S. Geological Survey Scientific Investigations Report 2016-5150, 74 p., 1 pl., https://doi.org/10.3133/sir20165150
Claassen, H.C., 1985, Sources and mechanisms of recharge for ground water in the west-central Amargosa Desert, Nevada; a geochemical interpretation: U.S. Geological Survey Professional Paper 712-F, 31 p., https://doi.org/10.3133/pp712F
Davis, K.W., Eldridge, W.G., Allander, K.K., Gardner, M.A., and Mayers, C.J., 2025, MODFLOW 6 groundwater flow models and supporting data for evaluation of stream capture related to groundwater pumping, middle Humboldt River Basin, Nevada (Provisional Release): U.S. Geological Survey data release, https://www.sciencebase.gov/catalog/item/6397944bd34e0de3a1f065e4
Halford, K.J., and Jackson, T.R., 2020, Groundwater characterization and effects of pumping in the Death Valley regional groundwater flow system, Nevada and California, with special reference to Devils Hole: U.S. Geological Survey Professional Paper 1863, 178 p., https://doi.org/10.3133/pp1863
Harbaugh, A.W., 2005, MODFLOW-2005, the U.S. Geological Survey modular ground-water model—the Ground-Water Flow Process: U.S. Geological Survey Techniques and Methods, book 6, chap. A16, variously paged, accessed June 27, 2017, at https://pubs.usgs.gov/tm/2005/tm6A16/
Hsieh, P.A., and Winston, R.B., 2002, User’s Guide To Model Viewer, A Program For Three-Dimensional Visualization of Ground-water Model Results: U.S. Geological Survey Open-File Report 02-106, 18 p. https://water.usgs.gov/water-resources/software/ModelViewer/
Jackson, T.R., and Halford, K.J., 2019, Estimation of groundwater flow through Yucca Flat based on a multiple-well aquifer test at well ER-6–1–2 main, Nevada National Security Site, southern Nevada: U.S. Geological Survey Scientific Investigations Report 2019–5038, 27 p., https://doi.org/10.3133/sir20195038
Walker, G.E., and Eakin, T.E., 1963, Geology and ground water of Amargosa Desert, Nevada-California: Nevada Department of Conservation and Natural Resources, Water Resources—Reconnaissance Series Report 14, 45 p., http://images.water.nv.gov/images/publications/recon%20reports/rpt14-Amargosa_valley.pdf