## Slide 1: Obtaining Useful Answers from Groundwater Models:    Uncertainty Analysis
Keith J Halford, Carson City, NV
Tracie Jackson, Henderson, NV

## Slide 2: Uncertainty & Decisions
Flow & transport models primarily guide decisions
  Estimate maximum extent of a plume
  Change in water levels from moving pumping (POD)
Inherently uncertain results, Models are greater than 90 percent fantasy by volume
Subset of decisions where formal uncertainty beneficial
  Occurs between empirically known responses and beyond reach of available data to inform
  Area between known and unknown also uncertain

## Slide 3: Data Density
Model results depends on data from
  Wells— Water levels, pumping, aquifer tests
  Springs — Pool altitudes & discharges
Influence extends from wells & springs
  Uncertainty greater away from points
  High-altitude springs add data, Reduces uncertainty, but amount debatable
Minimum distance from data algorithm illustrates subjectivity
  Points weighted equally, Not reasonable
  Need pair of points, Could be 1, 3, 4, etc.
  Distance to unknown debatable
Uncertainty in flow model similar
Ash
Meadows
Basin
Yucca Flat
LCA model
40 MILES

## Slide 4: Yucca Flat LCA model
Flow in carbonate rocks simulated
  Parsed rocks, faults, … are parameters
    Spatial extents vary greatly
    Recharge & leakage also parameters, 146 in all
  Objective function compares simulated to,
    15 steady-state water levels &
    Drawdowns in 5 wells from ER-6-1#2 aquifer test
    Controls calibration & uncertainty analysis
  Flow into northern Yucca Flat important
    Regional model defines flows to LCA model
    DVRFS.v1 error created fire hose, >10,000 acre-ft/yr
    DVRFS.v2 reduces to ~3,000 acre-ft/yr
    Granite & clastics, <300 acre-ft/yr† sensible
Parameter sensitivity, uncertainty analysis, & confidence intervals illustrated with LCA
5 MILES
(Navarro-Intera, LLC, 2013; fig. 5-28)
N
5 MILES
3 MILES
†(Winograd and Thordarson, 1975; Harrill and others, 1988)
ER-6-1#2

## Slide 5: Parameter Sensitivity
Changing sensitive parameter (knob), Changes objective function (SS)
  For example, increase T in major fault, Simulated water level decrease or Q increase
  Weighting in SS also affects sensitivities
Identifiability index scaled sensitivity
For parameters (knobs) in LCA model
  10%, Estimable—Clear change in SS
  20%, Changes similar to measurement error
  70%, Estimation delusional, No change in SS
  70% to 90% of knobs are in null space, because they do not significantly affect SS
Test uncertainty from insensitive knobs
(Navarro-Intera, LLC, 2013; fig. 5-39)
KNOWN
MAYBE
UNKNOWN

## Slide 6: Null-Space Monte Carlo (NSMC)
Change null-space (insensitive) parameters
  Randomly varied within expected ranges
  Revise all parameters so alternative or Monte-Carlo model is calibrated
  Computationally efficient, extra model run or two for each Monte-Carlo model
Examine uncertainty of a model result, For example, flow into N. Yucca Flat
  Sort from low to high; 1,400 to 10,300 acre-ft/yr
  Median & average ~3,500 acre-ft/yr
  95% confidence interval; 1,500 to 7,200 acre-ft/yr
Rigorously computed, but wrong
  Plausible estimates <300 acre-ft/yr
(Navarro-Intera, LLC, 2013; fig. 5-56)
95% confidence interval
Median ~3,500 acre-ft/yr
Just Wrong
Plausible estimates <300 acre-ft/yr
Winograd and Thordarson, ~40 acre-ft/yr (1975; pg. C93)

## Slide 7: Quantifiably Weak
Uncertainty analysis depends on objective function,
  Weights affect observation significance
  Not easily incorporated data missing, weight=0
“Looks funny…,” neglected information
  3,500 acre-ft/yr into N. Yucca Flat odd relative to total discharge ~20,000 acre-ft/yr
  Exact value difficult to estimate
  Can bound to less than 1,500 acre-ft/yr
Transmissivity estimates in 5 wells
  Consistent with PP712-C (1975)
  Not in carbonate & small volumes as counter
Disturbing result, but ancillary to purpose
20 MILES
Ash
Meadows
Basin
Spring
Mountains
2½
18
1½
3½

## Slide 8: Yucca Flat—Simulated Transport
Simulated tritium plume after 50 years
  Transport significant result
  Color flood shows probability of exceeding SDWA† standard; 20,000 pCi/L
Simplify to contours of 5%, 50%, and 95%
  5%, Unlikely maximum extent
  50%, Best estimate of extent
  95%, Almost guaranteed to exceed SDWA
Exceeds SDWA 0.8 mi south of Torrido
Well ER-7-1 drilled during 2003
  600 ft downgradient of Torrido
  Designed to measure plume
5 MILES
N
Probability of
exceedance,
in percent
95
5
50
N
1 MILE
Torrido
ER-7-1
50%, Best Guess–3.8 mi
95%, 0.8 mi, Super Certain
(Navarro-Intera, LLC, 2013; fig. 6-62)
†Safe Drinking Water Act (2017)

## Slide 9: Measured Tritium Concentrations
Torrido detonated May 1969
  Tritium concentrations decayed by 17 fold during 50 years
  Simulated concentrations exceed SDWA at well ER-7-1 during 2019
Tritium 117 pCi/L, July 2003; ER-7-1
  About 100 times less than SDWA limit
  Tritium 2 pCi/L in 2014, post peer review
Sampling appears to be better investment than uncertainty analysis
50 years after detonation
Yucca Flat peer review
Simulated
Reality
Tritium decay

## Slide 10: Multiple Wells
Tritium also measured in wells U-3cn-5 and UE- 7nS
  All wells within 600 ft of a nuclear test
  Tritium concentrations 10 to 1,000 times less than SDWA standard; 20,000 pCi/L
  Limited data more certain than model
NTS/NNSS closure program not fast or cheap
  Starts about 1991
  20 years between investigation plan & closure report for Yucca Flat
  Uncertainty consumed >10% of time
Tritium decay
Yucca Flat peer review
ER-12-1 drilled, first UGTA well
Plan for investigation (2000)
Closure report (2020)

## Slide 11: Best Estimate Needed
Weaknesses in transport analysis arose from,
  Propagating mistakes from supporting model to dependent model
  Neglecting difficult to quantify information
  Conflating best estimates and conservative estimates
    Properties that accelerate transport assumed
    Biased assumptions forgotten/ignored for uncertainty analysis
Uncertainty analysis better for targeting new data
  Absolute results from all models problematic
  Analyze change in uncertainty of drawdown or flow with new data
  Worth of predicted improvements depends on correctness of model

## Slide 12: Conclusions
Calibration & uncertainty analysis depend on judgement
  Obj. function — Data exclusion, data inclusion, & Weighting of included data
  Parameters — Spatial extents as faults, zones, or pilot points, Likely ranges once defined; reasonable or textbook?
Uncertainty analysis is not free, Can cost measuring useful data
“DUDE, you start looking at uncertainty, the uncertainty of the uncertainty, and you never get anything done.”
—Rich Niswonger, USGS

## Slide 13: References
Belcher, W.R., ed., 2004, Death Valley regional ground-water flow system, Nevada and California—Hydrogeologic framework and transient ground-water flow model: U.S. Geological Survey Scientific Investigations Report 2004-5205, 408 p., https://pubs.er.usgs.gov/publication/sir20045205
Halford, K.J., and Jackson, T.R., 2020, Groundwater characterization and effects of pumping in the Death Valley regional groundwater flow system, Nevada and California, with special reference to Devils Hole: U.S. Geological Survey Professional Paper 1863, 178 p., https://doi.org/10.3133/pp1863
Harrill, J.R., Gates, J.S., and Thomas, J.M., 1988, Major ground-water flow systems in the Great Basin region of Nevada, Utah, and adjacent states: U.S. Geological Survey Hydrologic Atlas 694-C, pls. 1–2. https://doi.org/10.3133/ha694C
Ludington, Steve, ed., 2006, Mineral Resource Assessment of Selected Areas in Clark and Nye Counties, Nevada: U.S. Geological Survey Scientific Investigations Report 2006–5197, 244 p., https://doi.org/10.3133/sir20065197
Navarro-Intera, LLC, 2013, Phase I flow and transport model document for Corrective Action Unit 97—Yucca Flat/Climax Mine, Nevada National Security Site, Nye County, Nevada, Rev. 1: Las Vegas, Nevada, Navarro-Intera Report N-I/28091-080, https://www.osti.gov/scitech/biblio/1094979
Theis, C.V., 1940, The source of water derived from wells—Essential factors controlling the response of an aquifer to development: Civil Engineering, v. 10, p. 277–280, https://water.usgs.gov/ogw/pubs/Theis-1940.pdf
Winograd, I.J., and Thordarson, W., 1975, Hydrologic and hydrochemical framework, south-central Great Basin, Nevada-California, with special reference to the Nevada Test Site: U.S. Geological Survey Professional Paper 712-C, p. C1–C126. https://doi.org/10.3133/pp712C