## Slide 1: Obtaining Useful Answers from Groundwater Models:    Application, Grids, & Reporting
Keith J Halford, Carson City, NV
Tracie Jackson, Henderson, NV

## Slide 2: Grid Effects ─●─ Minor Issue

## Slide 3: Differences
PMOV model inside DVRFS.v1
Sample T at aquifer tests from both models & compare to field results
Misfit of DVRFS.v1 to measured transmissivities greater than PMOV
More misfit, if field T < 1,000 ft²/d
  Bias consistent with expectations
  Low T areas neglected more without T observations in objective function
Misfits frequently attributed to coarse/regional grid, 1,500 m
NOT true, as will be demonstrated
50 MILESc
DVRFS.v1
PMOV

## Slide 4: Coarse Grid OK
Coarsen PMOV grid
  Cells originally 300 m on a side
  Revise to 1,500-m cells
Calibrate to,
  Water levels & transmissivity
Coarse grid explains data
Simulated water levels & transmissivities do not differ materially
Matching measured T not limited by 1,500-m grid
1,500-m
10 MILES

## Slide 5: Calibration Corrects
Compare near Oasis Valley
Maximum difference in T, a factor of 2
Simulated water table identical
Similar errors where water table near land surface
  Greater detail in 300-m DEM
  Causes nominally worse errors

## Slide 6: Grids & Pumping
Pumping
Point of Concern
Simulated pumping specifies discharge from a cell, e.g. Q = 500 gpm
  Truncation limited to pumped cell
  Heads affected to centers of surrounding cells, Interpolation
Grid refinement necessary where,
  Pumping and point of interest close
  Separated by a few cells

## Slide 7: Pumping Wells
Observations in pumping wells
Head in cell not equal to head in well
Δh cell to well from Thiem,
Equivalent outer radius, rO, is 0.2 ΔX
No transients in cell
  Good enough for analyzing long-term response
For example, drawdown in pumping well ~ 150 ft;
  Cell volume ~100,000 gal; ΔX=500 ft & S=0.00035
  If Q=500 gpm; 200 min or 3.3 hrs to void 500-ft cell
  OK for monthly pumping, not an 8-hr aquifer test
(Modified from Halford and Hanson, 2002)
hWELL
hCELL

## Slide 8: Grid-Scale Example
Hypothetical rectangular aquifer
Properties & boundaries
  500 ft thick; K is depth dependent
  Sy= 0.15 & Ss = 2x10¯⁶ 1/ft
  Vertical anisotropy is 10:1
  Discharge to 2 streams
Seasonal pumping
  3 wells, 4,800 acre-ft/yr
Two models of same system
Coarse model
  dX = 3,000 ft
  dZ = 100 ft
  30 Mb files
Fine model
  dX = 1,000 ft
  dZ = 50 ft
  490 Mb files

## Slide 9: Minimal Differences
No practical differences between coarse & fine
Predicted drawdowns differ less than 10%
Specified flow—Truncation error in pumped cell
2 MILES

## Slide 10: Quick & Simple
Grids should be generated quickly without excessive thought
  Rectangular grid for 1 model has advantage of simplicity
    Applies to creation & translating from XY >> Row-Column >> XY
    Adding child models complicates both creation & translation
  Quadtree grids also have well-defined structure, Relatively easy to modify
    Must search in 2D to translate from XY >> model node
Risk investment problem with complex unstructured grids
  For example, 1-2 years developing Yucca Flat grid
  LCA model too small to correctly analyze ER-6-1#2 aquifer test
  Wrote about model limitations, rather than revising model extent

## Slide 11: CONCLUSIONS
Results not overly sensitive to detail of model grid
  In addition to drawdowns, mass balance, stream capture, flow paths, & other results minimally affected by discretization
  Detailed grids frequently driven by aesthetics
Model run time & file sizes basic measure, not total cost
  Model should be run many 10,000s of times to calibrate
  Increasing model run time costs calibration as time runs short
Post-processing of results also affected as files swell

## Slide 12: Reporting ─●─ Keep looking, Show results clearly

## Slide 13: Reporting
Groundwater models, Flexible tools
  Better approximations
  Variability with depth
Complexity increasing
  Complex K distribution
  Uncertainty analysis leads to multiple realizations of K
  More to report
Synthesis needed
  Details exceed comprehension

## Slide 14: Input Reported
Vertical discretization
  Couple of sections shown
Geologic units
  Many maps with many zones per map
Tables of K, S, & Sy
Depth decay figure
33 figures & tables
K at 1 model cell defined
  Multiple geologic units
  Depth decay, from land surface
  Hydraulic-flow barrier
No clear picture
DVRFS.v1 (Belcher, 2004)

## Slide 15: Integrated Results
Revisit Death Valley, version 1
Map transmissivity
  K to model layers
  Apply depth decay
  Smear flow barriers
  Sum across layers
Big picture clear
  A few sins, but worthwhile
  Characterization of model results unaffected by simplifications
Computed from MODFLOW files, Pain and suffering

## Slide 16: Direct Comparison
Many aquifer tests around Nevada Test Site (NNSS)
Superimpose results
Transmissivity estimates
  Site specific information, rather than broad ranges
  Negate thickness difference
  More certain than K

## Slide 17: Looking Required
Land surface & water table
  Avoid deep lakes
  Hazards in DVRFS.v1
13,000 acre-ft/yr to N. Yucca Flat
Transmissivity
  Easy to see odd patches of high T
  High T below spring line of Ash Meadows, where thick clays occur

## Slide 18: CCRP— Input Only
Results 2008 review
  Most springs dry
  Many “lakes”
  Flow uphill between basins, in pink
  Transmissive playas, greater than 50,000 ft²/d
  Unlikely phreatophyte discharge, Pink drains above model
  Significant flow in deepest layer
Deficiencies from not looking
LAKES
TRANSMISSIVITY
INTERBASIN FLOW
DRAINS
DEEP FLOW
100 MILES
CCRP

## Slide 19: CCRP—Output
Results 2009 review
Discharges reported
Total transmissivity
  CCRP & DVRFS.v1 reported
  Overview & context
Conceptual disagreements persist, but parts shown
Details also provided
Central Carbonate Rock Province (SNWA, 2009)

## Slide 20: CCRP—Output Details
Cross-section for all rows
  Geologic units
  Computed hydraulic conductivity from HUF
  Simulated water levels
  Local plan view
  Horizontal flow barriers (HFB)
Hydraulic conductivity (K) in MODFLOW
  Mostly reported, except HFB
  Sins needed for HFB
Reporting comprehensible
Transmissivity knowable
Central Carbonate Rock Province (SNWA, 2009)
Geology
K, Hydraulic Conductivity
PLAN VIEW
K, in meters per day

## Slide 21: Demonstrate Benefit
Added details assumed to improve models
Complex models require
  More supporting information
  Longer model execution times
  Increased reporting demands
Money and time finite
  More unproven assumptions
  Degraded model calibration
  Incomplete reports
Demonstrate benefits
  Address specific weaknesses
  Prove added complexity improves answers

## Slide 22: Resources
Basic ground-water hydrology
  1983, Heath, Ralph C. USGS Water Supply Paper:2220
Ground Water And Surface Water A Single Resource
  1998, Winter, T.C., J.W. Harvey, O.L. Franke, and W.M. Alley, USGS Circular 1139
Guidelines for Evaluating Ground-Water Flow Models
  2004, Reilly, T.E. and A.W. Harbaugh USGS Scientific Investigations Report 2004-5038

## Slide 23: CONCLUSIONS
Models flexible—Answer many questions
Models improved by clear purpose
Data & questions should drive model complexity
  Additional data dispels ignorance, not more models
  Show added details improve answers
Clear ties to measurements increase confidence
Require complete reporting
  Interior of Earth can be mysterious,
  No aspect of a model should be mysterious

## Slide 24: References
Belcher, W.R., ed., 2004, Death Valley regional ground-water flow system, Nevada and California—Hydrogeologic framework and transient ground-water flow model: U.S. Geological Survey Scientific Investigations Report 2004-5205, 408 p., https://pubs.er.usgs.gov/publication/sir20045205
Belcher, W.R., Sweetkind, D.S., Faunt, C.C., Pavelko, M.T., and Hill, M.C., 2017, An update of the Death Valley regional groundwater flow system transient model, Nevada and California: U.S. Geological Survey Scientific Investigations Report 2016-5150, 74 p., 1 pl., https://doi.org/10.3133/sir20165150
Fenelon, J.M., Halford, K.J., and Moreo, M.T., 2016, Delineation of the Pahute Mesa–Oasis Valley groundwater basin, Nevada (ver. 1.1, May 2016): U.S. Geological Survey Scientific Investigations Report 2015–5175, 40 p., https://doi.org/10.3133/sir20155175
Halford, K.J., and Jackson, T.R., 2020, Groundwater characterization and effects of pumping in the Death Valley regional groundwater flow system, Nevada and California, with special reference to Devils Hole: U.S. Geological Survey Professional Paper 1863, 178 p., https://doi.org/10.3133/pp1863
Heath, R.C., 1983, Basic ground-water hydrology: U.S. Geological Survey Water Supply Paper 2220, 84 p. https://doi.org/10.3133/wsp2220
Navarro-Intera, LLC, 2013, Phase I flow and transport model document for Corrective Action Unit 97—Yucca Flat/Climax Mine, Nevada National Security Site, Nye County, Nevada, Rev. 1: Las Vegas, Nevada, Navarro-Intera Report N-I/28091-080, https://www.osti.gov/scitech/biblio/1094979
Peaceman, D.W., 1983, Interpretation of well-block pressures in numerical reservoir simulation with nonsquare grid blocks and anisotropic permeability: Society of Petroleum Engineers Journal, p. 531–543. https://www.osti.gov/biblio/5648463
Reilly, T.E., 2001, System and boundary conceptualization in ground-water flow simulation: U.S. Geological Survey Techniques of Water-Resources Investigations, Book 3, Chapter B8, 26 p. http://pubs.usgs.gov/twri/twri-3_B8/
Reilly, T.E. and A.W. Harbaugh, 2004, Guidelines for Evaluating Ground-Water Flow Models: U.S. Geological Survey Scientific Investigations Report 2004-5038, 37 p. https://doi.org/10.3133/sir20045038
Southern Nevada Water Authority, 2009, Transient numerical model of groundwater flow for the Central Carbonate Rock Province—Clark, Lincoln, and White Pine Counties Groundwater Development Project. Prepared in cooperation with the Bureau of Land Management: Southern Nevada Water Authority, Las Vegas, Nevada, 394 p.
Winter, T.C., Harvey, J.W., Franke, O.L., and Alley, W.M., 1998, Ground water and surface water – A single resource: U.S. Geological Survey Circular 1139, 79 p. https://doi.org/10.3133/cir1139